## Slide 1: PHITS
Multi-Purpose Particle and Heavy Ion Transport code System
title
Aug. 2018 revised
Guidance for hands-on exercise
Environmental radioactivity
Notes: PHITS講習会 入門実習

## Slide 2: Step 1
Define contamination source of Am-241
  Use RI source function
  Depth 3cm, Radius: 1m in soil
Calculate effective dose rate (Sv/h)
  Use [T-Track] with “multiplier”
  Sample of [T-Track] with “multiplier” is available in \phits\recommendation\H10multiplier
  To calculate effective dose, set multiplier ID=-203 (ISO irradiation) or -202 (AP irradiation).

## Slide 3: Results of Dose equivalent
Ground

## Slide 4: Step 2
Add Cs-137 contamination
  Check the plot. How does it change?
Calculate effective dose rate at 1 m above the ground
  Dose in a box... x:-10~10, y:-10~10, z: 90~100
  Hint: make another t-track with nx, ny, nz = 1
  Be careful of statistical error
    Increase ncasc if necessary
Challenging task ! (Please try if possible)

## Slide 5: Effective dose normalization hints
According to the manual [T-Track] section
  Output of [T-track] is (particle/cm^2/source)
  When RI source is used it is (particle/cm^2/sec)
  Coefficient of Multiplier is (pSv*cm^2)
Convert the unit of the result to (μSv/h)
Necessary for challenging task !

## Slide 6
1m of the height
1.1x10^-02 (uSv/h)

## Slide 7: Step 3
Change the source radius : 1 m -> 3 m -> 9 m
  Keep the contamination density (Bq/cm^3) constant
  Check if dose rate reaches constant
    Compare dose distribution in 3 cases
Change other source definitions (depth, isotope, activity ratio…)

## Slide 8: Result
1m of the height
2.0x10^-02 (uSv/h)
3 m
9 m
1m of the height
1.2x10^-01 (uSv/h)
Large source area is necessary to reach equilibrium

## Slide 9: Step 4
Source radius : 3m
Calculate dose when ground is covered with
  1cm Soil
  1 cm Fe
  1 cm Pb