## Slide 1: PHITS
variance reduction techniques to improve efficiency of calculation A
Multi-Purpose Particle and Heavy Ion Transport code System
August 2018 revised

## Slide 2: Contents of Lecture
[importance]
Geometry splitting and Russian Roulette
２．Neutron deep penetration calculation
３．Calculation of particle production in thin target
[forced collision]
１．Introduction

## Slide 3: Neutron deep penetration calculation
14 MeV neutron
Calculate neutron transport in thick shield
and dose rate distribution to depth
Execute “imp.inp” and measure computational time
Number of history: 1,500
you can find CPU time in phits.out “total CPU time”.
Concrete
50cm radius x 180 cm thick cylinder
Air
Effective dose is obtained by multiplying neutron fluence by dose conversion coefficient in PHITS.
[ P a r a m e t e r s ]
icntl = 0
maxcas = 8000
maxbch = 1
...
[ T - T r a c k ] (3rd)
mesh = xyz
…
axis = xz
z-txt = Effective dose [pSv/source]
file = imp-dose-xz.out
part = neutron
epsout = 1
gshow = 1
multiplier = all
mat mset1
all ( 1.0 -202 )
imp.inp

## Slide 4: Calculation of effective dose
4
[ T - T r a c k ] (2nd and 3rd )
…
multiplier = all
mat mset1
all ( 1.0 -202 )
(C k):
C normalization factor
k ID number
Dose with pSv unit is calculated when fluence is normalized by source intensity
Please see manual for the [multiplier] section
ID number | Dose conversion coefficient pSv cm2
-200 | H*(10)
-201 | Effective dose based on ICRP60 (AP irradiation)
-202 | Effective dose based on ICRP103 (AP irradiation)
-203 | Effective dose based on ICRP103 (ISO irradiation)
Excerpt of data for dose conversion coefficient in /phits/data/multiplier
In this time, source intensity is not used in the normalized factor C.
Fluence (1/cm2/source) x Dose conversion coefficient (pSv・cm2) = Dose (pSv/source)
Source intensity
Dose conversion coefficient
Fluence calculated by [t-track] can be multiplied with several functions that are pre-defined or defined in [multiplier] section

## Slide 5: Neutron deep penetration calculation
Number of history= 8,000
Need to improve the efficiency of Monte Carlo simulation!
Use variance reduction techniques
Normal calculation using a single CPU (Intel Core i5-4590 CPU @ 3.30GHｚ)
Number of history= 500,000
total cpu time = 6.39 sec
total cpu time = 215.36 sec
imp-dose-xz.eps
imp-dose-xz.eps

## Slide 6: Concept of weight in Monte Carlo calculation
Example：track length tally
Weight： Importance of the particles in Monte Carlo simulation
is always 1 in normal calculation*
Artificially increase the probability of rare event occurrences.
Frequency distribution per a history cannot be calculated,
e.g. [t-deposit] with output = deposit, NO MORE event generator!
*Not the case for low-energy neutron transport simulation
Li: track length of i-th particle
Wi: weight of i-th particle
n0: total history number

## Slide 7: Contents of Lecture
[importance]
Geometry splitting and Russian Roulette
２．Neutron deep penetration calculation
３．Calculation of particle production in thin target
[forced collision]
１．Introduction

## Slide 8: Cell Importance Method
Set important I to each cell. When a particle passes through the boarder of cell 1 and cell 2, set I2/I1
I2/I1>1: Particle split
I2/I1<1: Russian Roulette
killed or alive
W=1
W=1/3
W=1/3
W=1/3
I1=1
I2=3
e.g. I2/I1 is integer.
I2/I1 = 3: Always split into 3
I2/I1 is not an integer
I2/I1 = 2.75:
Split into 3 by 75%
Split into 2 by 25%
W=3
W=1
I1=1
I2=1/3
1/3 probability
2/3 probability
killed

## Slide 9: Check the Trajectory of Single Particle
Execute “imp-hist.inp”, and check the neutron trajectory
Importance for all cells is set to 1.0 in the default setting
I10=1.0
I1=1.0
I2=1.0
Air
Concrete
（R= 20cm，
Depth = 8cm×2）
imp-trajectory.eps
5MeV
Neutron
imp-hist.inp
[importance]
part = neutron
reg imp
10 1
1 1
2 1

## Slide 10: Let’s Increase Importance
imp-hist.inp
[importance]
part = neutron
reg imp
10 1
1 2
2 4
divided into 2 neutrons here
Reaction occurs here
I10=1
I1=2
I2=4
imp-trajectory.eps

## Slide 11: Let’s Decrease Importance
imp-hist.inp
[importance]
part = neutron
reg imp
10 1
1 1/2
2 1/4
I10=1
I1=1/2
I2=1/4
imp-trajectory.eps
1/2 neutron survives
1/2 neutron is killed

## Slide 12: Let’s Increase Importance EXTREMELY!
imp-hist.inp
[importance]
part = neutron
reg imp
10 1
1 2
2 100
I10=1
I1=2
I2=100
imp-trajectory.eps
“A Sample Problem for Variance Reduction in MCNP” LA-10363-MS DE86 004380
It is better to set 2~3 for max importance ratio between neighboring cells.
Particles are divided too much
You waste your machine time without improving statistics!

## Slide 13: Example of calculation using [importance]
[importance]
part = neutron
reg imp
1 2.5**0
2 2.5**1
3 2.5**2
4 2.5**3
5 2.5**4
6 2.5**5
7 2.5**6
8 2.5**7
9 2.5**8
10 2.5**9
11 2.5**10
12 2.5**11
Thickness of 1 cell is 15 cm
Ii+1/Ii = 2.5
Activate the [importance] section in “imp.inp”, and execute PHITS
14 MeV neutron
Concrete:
50cm radius x 180 cm thick cylinder, 15cm thick cell x 12
14MeV neutrons with 1cm radius incidence along with z axis
total history = 1,500

## Slide 14: Example of calculation using [importance]
total history = 8,000
3.30GHz, single
[importance] off
More neutrons penetrate to deeper locations
total cpu time = 6.39 sec
・Check statistical uncertainty
Red:1.0, Yellow: ~0.1, Green: ~0.01
[importance]
total cpu time = 48.39 sec
imp-dose-xz.eps
imp-dose-xz_err.eps
1
Dose
Relative error

## Slide 15: Example of calculation using [importance]
Dose rate in each cell (15 cm thickness)
Original data：imp-dose-reg.out
15
With importance
Without importance

## Slide 16: Important Notice of Setting [importance]
1
2
4
8
16
32
1
1
8
8
8
32
Good example
Bad example
It is better to set 2~3 for max importance ratio between neighboring cells.
source
Reference:
“A Sample Problem for Variance Reduction in MCNP” LA-10363-MS DE86 004380
Large ratio among cells cause many particle splits.

## Slide 17: Bad Example for using [importance]
Bad example:
Very large importance gap between cell 5 & 6
Relative errors are too large in comparison to previous setting!
[importance]
part = neutron
reg imp
1 2.5**0
2 2.5**0
3 2.5**0
4 2.5**0
5 2.5**0
6 2.5**5
7 2.5**6
8 2.5**7
9 2.5**8
10 2.5**9
11 2.5**10
12 2.5**11
Let’s try a bad example!
imp-dose-xz.eps
imp-dose-xz_err.eps

## Slide 18: Contents of Lecture
[importance]
Geometry splitting and Russian Roulette
２．Neutron deep penetration calculation
３．Calculation of particle production in thin target
[forced collision]
１．Introduction

## Slide 19: What is forced collision?
Radiation is forced to collide with a very thin target (film).
10μm thick Si
100MeV proton
Example of application： Simulation of particle production measurements with a film
10μm thick Si
without forced collision：
No collision occurred in such thin target.
with forced collision：
Proton always collide with Si.

## Slide 20: Simulation of particle production measurements with a film.
[t-product]: energy distribution of alpha and Si produced in a target → true cross section
[t-cross]：energy distribution of alpha and Si in a detector → measured cross section
force.inp
Without forced collision: protons do not collide with a film.
maxcas = 5000
maxbch = 5
product.eps
Radius 0.5cm, 10μm thick Si
100MeV proton
detector
void
cross.eps
Let’s execute force.inp

## Slide 21: Forced collision
The forced collision is useful for analyzing secondary particles generated from a thin target
Split into two particles
Forced collision cell
Weight of uncollided particle：Wi×exp(-Sd)
Collided particle
Incoming weight Wi
S: macroscopic cross section
Collide position is decided by cross section at random.
d: distance across cell
Uncollided particle
Weight of collided particle：
Wi×{1-exp(-Sd)}
fcl: Forced collision factor (normally, fcl = -1)
fcl = -1: applies only to particles entering the cell (weight cut-off is not applied)
fcl = 1: applies to all particles surviving weight cutoff (weight cut-off is applied)
Method of forced collision decreases history variance, but calculation time per history increases.

## Slide 22: Let’s force particles to collide with a film
force.inp
Tally information in a film at particle production
cross.eps
[Forced Collisions] off
part = proton
reg fcl
1 -1.0
forced collision
track-xz.eps
Weight of particles produced by forced collision are below weight cutoff, wc2.
⇒ It is hard to transport secondary particles due to Russian Roulette.
α
Delete off and execute it
product.eps

## Slide 23: How to transport secondaries produced by forced collision?
force.inp
[parameters]
……….
wc2(1) = 1.0E-12 # weight cutoff of proton
wc2(18) = 1.0E-12 # weight cutoff of Alpha
wc2(19) = 1.0E-12 # weight cutoff of Nucleus
To transport secondaries produced by forced collision,
Let’s set a small number on weight cutoff, wc2.
α
track-xz.eps
Si
This experiment can not measure Si production cross sections correctly
because many Si are stopped within a target.
cross.eps
product.eps

## Slide 24: Summary
Cell importance method is effective in deep penetration calculations.
Ratios of importance between neighboring cells are better to be less than 3
→ Appropriate setting of [importance] is very important.
It is better to use Weight Window Generator
for complicated geometry (weight B).
Forced collision method is effective to calculate particle production in a thin target.