## Slide 1: PHITS
variance reduction techniques to improve efficiency of calculation B
Multi-Purpose Particle and Heavy Ion Transport code System
title
August 2018 revised

## Slide 2: Contents of Lecture
[weight window]
Weight windows
[weight window generator]
Function to automatically generate [weight window]
Neutron deep penetration calculation

## Slide 3: Concept of weight in Monte Carlo calculation
Example：track length tally
Weight： Importance of the particles in Monte Carlo simulation
is always 1 in normal calculation*
Artificially increase the probability of rare event occurrences.
Frequency distribution per a history cannot be calculated,
e.g. [t-deposit] with output = deposit, NO MORE event generator!
*Not the case for low-energy neutron transport simulation without e-mode.
Li: track length of i-th particle
Wi: weight of i-th particle
n0: total history number

## Slide 4: Difference between cell importance and weight window methods
“Cell importance method” assign a single value of weight to each cell.
“Weight window method” assign allowed weight range (window) to each cell and to each energy group.
Efficient simulation with focusing on the important energy region, such as high-energy neutron.
WL=0.5
Weight
W1=1
Weight
I1=1
I2=3
W2=1/3
Number of particle 1 →
I2/I1=3
energy group1
region1
WU=2.5
WL=0.25
WU=1.25
region2
energy group2
W=1
WL=0.5
Weight
WU=2.5
WL=0.17
WU=0.85
W1=1
W2=0.5
1→
W1/W2=2
Number of particle 1 → 1
Cell importance method
Weight window method
region1
region2
region1
region2

## Slide 5: Parameters Related to Weight Window
wupn: Ratio of upper to lower limits of allowed weight (D=5.0)
mxspln: Maximum number of split per event (D=5.0)
mwhere: Timing for considering weight window (D=0)
-1: reaction, 0: both, 1: surface crossing
These parameters are defined in [parameters] section.
See manual “4.2.4 Cut off time, cut off weight, and weight window” for more detail.

## Slide 6
Let’s execute “weight-hist.inp”, and check the neutron trajectory
weight-trajectory.eps
Air
Water
（r= 10cm，
Depth = 5cm×2）
5MeV
neutron
Check the Trajectory of Single Particle

## Slide 7: Set [Weight Window] Section
Weight of neutron is within the weight window range -> No split or no Russian roulette
Activate the 1st [weight window] section in weight-hist.inp, and execute PHITS!
[weight window]
part = neutron
reg ww1
1 0.25
2 0.25
WL=0.25
Weight
Cell 1
WU=5 x WL =1.25
WL=0.25
W1=1
Cell 2
Set value in each region
Same weight window for all energies
Lower limit of allowed weights, WL, of each cell is defined in [weight window]
Upper limit of allowed weights, WU, is automatically set to WL x wupn (D=5)
weight-trajectory.eps
weight-hist.inp

## Slide 8: Let’s Decrease Weight Window in Cell 2
WL=0.25
Weight
Cell 1
WU=1.25
WL=0.125
WU=0.625
W1=1
Cell 2
Decrease the lower limit of allowed weights in cell 2, and execute PHITS!
Particle Split
Neutron is divided into 2 because its weight (=1) is higher than the upper limit (=0.625)
[weight window]
part = neutron
reg ww1
1 0.25
2 0.125
weight-hist.inp
weight-trajectory.eps

## Slide 9
WL=0.25
Weight
Cell 1
WU=1.25
WL=0.005
WU=0.025
W1=1
Cell 2
The ratio of max weight window between neighboring cells should be 2~3
Neutrons are divided into mxspln(D=5) every time (crossing surface or reaction)
[weight window]
part = neutron
reg ww1
1 0.25
2 0.005
weight-hist.inp
weight-trajectory.eps
Let’s Decrease Weight Window in Cell 2 EXTREMELY!
Decrease the lower limit of allowed weight in cell 2 EXTREMELY, and execute PHITS!

## Slide 10: Set different Weight Window for Each Energy Group
weight-hist.inp
[weight window]
part = neutron
eng = 2
0.01 1.0e5
reg ww1 ww2
1 0.25 0.25
2 0.125 0.125
Let’s “off” the 1st [weight window], and
activate the 2nd one & execute PHITS
W1=1
WL=0.25
Weight
Cell 1
WU=1.25
WL=0.125
WU=0.625
Cell 2
Particle Split
E < 0.01 MeV
W1=1
WL=0.25
Weight
Cell 1
WU=1.25
WL=0.125
WU=0.625
Cell 2
Particle Split
0.01 MeV < E < 105MeV
2 energy groups are defined
But the weight window are the same for each group
weight-trajectory.eps
Maximum energy for each group
Neutron is divided into 2 because its weight (=1) is higher than the upper limit (=0.625)
(Same as 2 pages before)

## Slide 11: Increase Weight Window Only for Low-Energy Neutrons
Reduce low-energy neutron transport,
and focus on high-energy neutron transport
Get poor and better statistics at shallower and deeper locations, respectively
weight-hist.inp
Increase weight window for low-energy neutrons by 10, and execute PHITS
[weight window]
part = neutron
eng = 2
0.01 1.0e5
reg ww1 ww2
1 0.25*10 0.25
2 0.125*10 0.125
W1=1
WL=2.5
Weight
Cell 1
WU=12.5
WL=1.25
WU=6.25
Cell 2
Russian
Roulette
E < 0.01 MeV
W1=1
WL=0.25
Weight
Cell 1
WU=1.25
WL=0.125
WU=0.625
Cell 2
Particle Split
0.01 MeV < E < 105MeV
Low-energy neutron is killed
weight-trajectory.eps

## Slide 12
Geometry, source, history are the same as imp.inp
[weight window]
set: c10[1.0]
part = neutron
eng = 2
1.0e-3 1e5
reg ww1 ww2
1 c10*2.5**(-1) 2.5**(-1)
2 c10*2.5**(-2) 2.5**(-2)
3 c10*2.5**(-3) 2.5**(-3)
・・・
Cylindrical Concrete
(r = 50cm, depth = 1.8 m)
Thickness of each cell = 15 cm
Execute PHITS using weight.inp, and check your CPU time
Decrease weight window of neighboring cells by 1/2.5 for particle split
Set same weight window for all energy groups (because c10=1.0)
14MeV
neutron
weight-dose-xz_err.eps
weight-dose-xz.eps
weight.inp
Example of calculation using [weight window]
total cpu time = 18.62 sec

## Slide 13
Increase the weight window for low-energy neutrons by 10, and execute PHITS
Most low-energy neutrons are immediately killed when produced because of Russian Roulette
Range of low-energy neutrons is short, therefore statistical uncertainty in the depth changes very slightly
total cpu time = 18.62 ->
[weight window]
set: c10[10.0]
part = neutron
eng = 2
1.0e-3 1e5
reg ww1 ww2
1 c10*2.5**(-1) 2.5**(-1)
2 c10*2.5**(-2) 2.5**(-2)
3 c10*2.5**(-3) 2.5**(-3)
・・・
weight.inp
weight-dose-xz_err.eps
weight-dose-xz.eps
Example of calculation using [weight window]
7.47 sec

## Slide 14: Comparison of CPU time
Use [weight window]; same value for all energies
Use [importance]
Normal calculation (No [importance], No [weight window])
Use [weight window]; different values for low- and high-energy neutrons
total cpu time = 48.39 sec
total cpu time = 6.39 sec
total cpu time = 18.62 sec
total cpu time = 7.47 sec

## Slide 15: Dose Reduction Rate in Concrete
You can improve the efficiency of your calculation by appropriately setting weight window for each neutron energy group
90 cm
Dose profiles obtained in various setting agree well except beyond region #8

## Slide 16: Contents of Lecture
[weight window]
Weight windows
[weight window generator]
Function to automatically generate [weight window]
Neutron deep penetration calculation

## Slide 17: Weight Window Generator [T-WWG]
Tally to generate appropriate weight window automatically in each cell
The weight window is given by the flux in each cell normalized by the maximum flux.
If the flux is zero, weight window is supplemented with a finite small value.
This procedure applies to each particle and energy bin.
mesh=reg and xyz because [weight window] allows mesh=reg and xyz.
[ T - WWG ]
mesh = reg
reg = {1-12}
part = neutron
e-type = 1
ne = 2
0 0.01 1e5
axis = wwg
file = WWG.out
To generate the weight window, track length of particle normalized by a volume in each cell is calculated (flux: 1/cm2). Same method with [t-track].
For mesh=reg, it is necessary to define cells volumes by [volume] section.
For mesh=xyz, volume in each region is calculated automatically.
【Procedure of automatic generation】

## Slide 18: Divide weight window region with region mesh
mesh=reg is available for [T-WWG] in WWG.inp.
100 cm radius x 180 cm thick cylinder
weight-dose-xz.eps
Execute “WWG.inp” and check geometry.
WWG.inp
Weight window region is divided by region defined in [cell]section.
[ T - WWG ]
mesh = reg
reg = {1-12}
part = neutron
e-type = 1
ne = 2 $ 2 energy bin
0 0.01 1e5
axis = wwg
file = WWG.out

## Slide 19: Particle transport calculation with region mesh in T-WWG
Let’s execute 1st particle transport calculation and check trajectory of neutrons and initial values of the weight window.
[ Weight Window ]
mesh = reg
set: c71[0.0] c72[c71+6.18192E-08] c73[4.05443E-05]
set: c74[0.0] c75[c74+3.62115E-08] c76[4.92671E-05] part = neutron
eng = 2
1.00000E-02 1.00000E+05
reg ww1 ww2
1 (2.82289E-05+c71)/c73 (4.92671E-05+c74)/c76
2 (4.05443E-05+c71)/c73 (3.19182E-05+c74)/c76
3 (2.62727E-05+c71)/c73 (1.44445E-05+c74)/c76
4 (1.57704E-05+c71)/c73 (5.69405E-06+c74)/c76
5 (7.57407E-06+c71)/c73 (1.90163E-06+c74)/c76
6 (2.19087E-06+c71)/c73 (4.12666E-07+c74)/c76
7 (7.66554E-07+c71)/c73 (2.08198E-07+c74)/c76
8 (3.21984E-07+c71)/c73 (3.62115E-08+c74)/c76
9 (8.12275E-08+c71)/c73 (0.00000E+00+c75)/c76
10 (6.18192E-08+c71)/c73 (0.00000E+00+c75)/c76
11 (0.00000E+00+c72)/c73 (0.00000E+00+c75)/c76
12 (0.00000E+00+c72)/c73 (0.00000E+00+c75)/c76
WWG gives minimum value in the cell where flux is zero.
WWG.out
Initial values of the weight window
weight-dose-xz_err.eps
Without weight window
Execute PHITS with icntl=0
Maximum flux
Minimum flux

## Slide 20: Particle Deep Penetration Calculation with WWG
Method for efficient deep penetration of particles using results of [t-WWG]
In the 1st transport calculation, the initial weight window is generated by [t-WWG].
In the 2nd, the weight window is updated by initial values of weight window.
After the 3rd, calculations are repeated until particles are transported to depth, and appropriate weight window setting is eventually obtained.
After checking the weight window, adjust the total history.

## Slide 21: Particle transport calculation with region mesh in T-WWG
Activate the infl: {WWG.out} in “WWG.inp”, and execute the 2nd calculation
Use the 1st weight window
weight-dose-xz_err.eps
“WWG.out” is updated every execution
There is no region with zero flux.
WWG.out
The weight window obtained by the 2nd calculation
[ Weight Window ]
mesh = reg
set: c71[0.0] c72[c71+3.70089E-09] c73[4.09008E-05]
set: c74[0.0] c75[c74+5.12459E-10] c76[5.14770E-05]
part = neutron
eng = 2
1.00000E-02 1.00000E+05
reg ww1 ww2
1 (2.71604E-05+c71)/c73 (5.14770E-05+c74)/c76
2 (4.09008E-05+c71)/c73 (3.17957E-05+c74)/c76
3 (3.21450E-05+c71)/c73 (1.52164E-05+c74)/c76
4 (1.67049E-05+c71)/c73 (5.81886E-06+c74)/c76
5 (6.86253E-06+c71)/c73 (2.09567E-06+c74)/c76
6 (2.56029E-06+c71)/c73 (7.57085E-07+c74)/c76
7 (8.47601E-07+c71)/c73 (2.57661E-07+c74)/c76
8 (3.49091E-07+c71)/c73 (7.76580E-08+c74)/c76
9 (1.36336E-07+c71)/c73 (2.05946E-08+c74)/c76
10 (3.84463E-08+c71)/c73 (4.81371E-09+c74)/c76
11 (1.23612E-08+c71)/c73 (1.42294E-09+c74)/c76
12 (3.70089E-09+c71)/c73 (5.12459E-10+c74)/c76

## Slide 22: Particle transport calculation with region mesh in T-WWG
Let’s execute 3rd calculation and check distribution in depth and radial directions.
As the same weight window is used in each cell,
transverse flux distribution is inhomogeneous.
weight-dose-xz_err.eps
weight-dose-reg.eps
Use the 2nd weight window.
“WWG.out” is updated every execution.
Dose reduction rate in concrete
＊Statistics of photon dose in depth is not enough because WWG is not applied to photons.

## Slide 23: Divide weight window region with xyz mesh
[ T - WWG ]
mesh = xyz
x-type = 2
xmin = -100
xmax = 100
nx = 5
y-type = 2
ymin = -100
ymax = 100
ny = 5
z-type = 2
zmin = 0
zmax = 180
nz = 12
…
WWG2.inp
x,y: devide WWG region (-100 – 100 cm) into 5 layers at intervals of 40 cm
z: devide WWG region (0 – 180 cm) into 12 layers at intervals of 15 cm
xyz mesh is also available for [T-WWG] in WWG2.inp
6MeV
neutron

## Slide 24: Particle transport calculation with xyz mesh in T-WWG
WWG2.out
weight-dose-xz_err.eps
Without weight window
Let’s execute 1st particle transport calculation and check trajectory of neutrons and initial values of the weight window.
xyz mesh ID(i j k)
i=1,...,5,
j=1,...,5,
k=1,...,15
[ Weight Window ]
……
set: c71[0.0] c72[c71+6.80649E-09] c73[5.43047E-04]
set: c74[0.0] c75[c74+3.50813E-09] c76[1.02250E-03]
part = neutron
eng = 2
1.00000E-02 1.00000E+05
xyz ww1 ww2
(1 1 1) (0.00000E+00+c72)/c73 (0.00000E+00+c75)/c76
(1 1 2) (0.00000E+00+c72)/c73 (1.04175E-06+c74)/c76
(1 1 3) (5.59799E-08+c71)/c73 (0.00000E+00+c75)/c76
(1 1 4) (0.00000E+00+c72)/c73 (0.00000E+00+c75)/c76
(1 1 5) (0.00000E+00+c72)/c73 (0.00000E+00+c75)/c76 ……

## Slide 25: Particle transport calculation with xyz mesh in T-WWG
weight-dose-xz_err.eps
Without weight window
In [parameters] section, let’s increase “maxbnk”, which is the number of particles PHITS can store temporary.
*forced termination
if warnings are appeared Intermittently
Let’s enable infl: {WWG2.out} and execute 2nd and 3rd calculations.
Warning due to too many particles
Small weight window values are assigned to the regions where photon did not come.
In that case, particles are unexpectedly split in such regions
and it takes long time for calculations due to increasing physical memory used in PHITS.

## Slide 26: Particle transport calculation with xyz mesh in T-WWG
increase maxbnk by 100 times.
Let’s increase the bank array in WWG2.inp, and execute 2nd and 3rd calculation.
[ P a r a m e t e r s ]
icntl = 0
maxcas = 1500
maxbch = 1
negs = -1
file(1) = c:/phits
file(6) = phits.out
maxbnk = 10000

## Slide 27: Particle transport calculation with xyz mesh in T-WWG
[ P a r a m e t e r s ]
icntl = 0
maxcas = 1500
maxbch = 1
negs = -1
file(1) = c:/phits
file(6) = phits.out
maxbnk = 10000*100
weight-dose-xz_err.eps
Let’s increase the bank array in WWG2.inp, and execute 2nd and 3rd calculation.
Results of 2nd calculation
Results of 3rd calculation
Divide weight window regions into xyz direction
to achieve good statistics in all regions

## Slide 28: Exercise 1
WWG2.inp
[ T-track ] off
mesh = xyz
x-type = 2
xmin =
xmax =
nx = 1
y-type = 2
ymin = -10
ymax = 10
ny = 1
z-type = 2
zmin =
zmax =
nz = 1
…
Let’s set a tally region A (x=60-80 cm, y=-10-10 cm, z=0-20 cm)
using the second [T-track] tally (file = weight-dose-z.out)

## Slide 29: Answer 1
WWG2.inp
Let’s set a tally region A (x=60-80 cm, y=-10-10 cm, z=0-20 cm)
using the second [T-track] tally (file = weight-dose-z.out)
[ T-track ]
mesh = xyz
x-type = 2
xmin = 60
xmax = 80
nx = 1
y-type = 2
ymin = -10
ymax = 10
ny = 1
z-type = 2
zmin = 0
zmax = 20
nz = 1
…

## Slide 30: Exercise 2
Change maxbch=50 to increase the number of history
Set stdcut=0.1 in the 2nd [T-track] tally, and execute calculation
Check effective dose of neutrons with output of the 2nd [T-track] tally
(file = weight-dose-z.out)
WWG2.inp
[ P a r a m e t e r s ]
icntl = 0
maxcas = 1500
maxbch = 1
……
Increase the number of history and check effective dose for neutrons
[ T-track ]
…
file = weight-dose-z.out
stdcut =
…
*stdcut: When all relative values of STD (standard deviation) of the tally result are smaller than
stdcut at the last of one batch, PHITS finishes its calculation

## Slide 31: Answer 2
WWG2.inp
[ P a r a m e t e r s ]
icntl = 0
maxcas = 1500
maxbch = 50
x: z[cm]
y: Effective dose (pSv/source)
p: xlin ylog afac(0.8) form(0.9)
h: n x y(neutron ),hh0l n
# z-lower z-upper neutron r.err
0.0000E+00 2.0000E+01 3.7062E-04 0.0994
weight-dose-z.out
weight-dose-xz_err.eps
[ T-track ]
file = weight-dose-z.out
stdcut = 0.1
…
Increase the number of history and check effective dose for neutrons

## Slide 32: Summary
It is convenient to read output file of [t-WWG]（= [weight window] section） by the infl command in the 2nd and subsequent calculation.
[t-WWG] generates appropriate weight window automatically in each cell and energy.
Definition of cell volume by [volume] section is mandatory to use weight window.
The weight window is given by the flux in each cell normalized by the maximum flux.
“Weight window method” assigns allowed weight range (window) for each cell and each energy group.
Increase “maxbnk” when warning messages due to “too many secondary particle” appears.