## Slide 1
Basic Lecture I:
Geometry and Source Definition
title
May 2021 revised
Notes: PHITS講習会 入門実習

## Slide 2: Purpose of This Lecture
Purpose
Learn input format of PHITS, and how to define a simple geometry and a source term
You can obtain such results at the end of this lecture
(Particle fluence around a cylindrical water tank irradiated by a 290-MeV proton beam)

## Slide 3
General Description
Geometry
Source
Summary and Homework
Contents
Table of Contents
General definition
How to define cells
Definitions of boxes and cylinders
How to add materials
Geometry drawing software
Notes: 「実習」 前の基本的な話から

## Slide 4: Format of PHITS input
General description
Calculation conditions are specified by a text file
Basic format
keyword（parameter） = value or character
[ Section Name ] ←start of the section
An input file consists of several sections
(“space” means nothing)
parameter1 parameter2 parameter3 …
Parameters are separated by “space”
Up to 200 characters in one line
Lines starting with more than 6 spaces are successive lines
or
Parameters can be given in mathematic equations: e.g. 1.0+exp(-2.0)
Notes: 所謂「PHITS言語」
角括弧（：大カッコ←最近では望ましくない呼び名らしい。）

## Slide 5: Input support command
*Sections can be placed in an arbitrary order
[ ]off
skip this section
qp:
skip from this line to the next section
q:
equivalent to [end] section
Comment marks
C in the first 5 column of a line (except [material] section)
$ and # in the middle of a line
(but avoid using # in the [cell] and [surface] sections)
→$ is recommended
General description
Characters are case insensitive

## Slide 6: Main components of input
General description
Three fundamental components
See input example “lec01.inp”
In PHITS simulations, geometry in 3-dimensional virtual space and information on source particles are both essential to tally various quantities of the particles.
⇒ ① Geometry
② Source
③ Tally
Notes: この三大要素をテキストで表現しないといけない。

## Slide 7: Sample input
[Title]
title comments
[Parameters]
define parameters
[Source]
define source
[Material]
define materials
[Surface]
define surfaces
[Cell]
define cells
[T-Track]
track length tally
[T-3dshow]
3d show tally
[End]
This file consists of 9 sections.
② Source
Production of particles
① Geometry
Definition of 3D virtual space
③ Tally
Observation of quantities
General description
lec01.inp

## Slide 8: Output Files
General description
batch.out: batch information → Basic lecture III
phits.out: Calculation summary
track_xz.eps: Picture of particle trajectories
track_xz.out: Numerical data of particle trajectories
track_xz_err.eps: Picture of statistical uncertainties
track_xz_err.out: Numerical data of statistical uncertainties
Basic
Lecture
II
Terminal output
Input file name
Calculation progress and time
(Error information is shown up in this screen)

## Slide 9: Result of the sample input
General description
track_xz.eps
phits.out
Visualization of the result
Summary of the calculation
Version Number

## Slide 10
General description
phits.out
PHITS Logo + Version information
Input Echo
  Echo of the parameters specified in the input file
  Description of the parameters and their default values
Memory status
  You can check how many memories are used in the calculation
Batch information (You will learn about “Batch” in Lecture 3)
Summary of PHITS simulation
  Numbers of events such as source generation and nuclear reaction occurred
  Information on transported particles
  Numbers of secondary particles
  CPU time
  Numbers of library data access and use of reaction models
Output File
Error information is mostly given in the console Window,
but occasionally in the output file!

## Slide 11: List of “section”
General description
※See PHITS manual Sec. 5
Section name
[title]
[parameters]
[source]
[material]
[surface]
[cell]
[transform]
[temperature]
[mat time change]
[magnetic field]
[electro magnetic field]
[delta ray]
[track structure]
Section name
[super mirror]
[elastic option]
[frag data]
[importance]
[weight window]
[forced collisions]
[volume]
[multiplier]
[mat name color]
[reg name]
[counter]
[timer]
[end]
Notes: 実際の実験条件を忠実に再現できるように様々なセクションが用意されている。

## Slide 12: List of tally
Several tallies can be defined in one calculation to obtain various information on the particle transport.
*See manual sec. 6 for each tally section.
General description
Section name
[t-track]
[t-cross]
[t-point]
[t-deposit]
[t-deposit2]
[t-yield]
[t-product]
[t-dpa]
[t-let]
[t-sed]
Section name
[t-time]
[t-interact]
[t-dchain]
[t-wwg]
[t-wwbg]
[t-userdefined]
[t-gshow]
[t-rshow]
[t-3dshow]
Notes: 興味のある物理量を得ることに適したTally（検出器）が用意されている。

## Slide 13
General Description
Geometry
Source
Summary and Homework
Contents
Table of Contents
General definition
How to define cells
Definitions of boxes and cylinders
How to add materials
Supporting software
Notes: 「実習」 前の基本的な話から

## Slide 14: General definition
Geometry (General definition)
To make a 3-dimensional geometry, follow these three steps:
1) Define materials in [Material]
2) Define surfaces of cells in [Surface]
3) Define cells with materials in [Cell]
Water(H2O)
Aluminum (Al)
sphere surface
cuboid surface
water sphere
aluminum cuboid
water cylinder
Combine
cylinder surface

## Slide 15
Geometry (General definition)
15
You can use an infinite space.
X
Y
Z
But, void or air regions have to be defined explicitly. Furthermore, the outer boundary of the virtual space “outer void” has to be defined.
outer void
void
or air
3D virtual space
3D virtual space in PHITS consists of cells defined in XYZ coordinate system.
Notes: XYZ座標系（無限に広がる空間）

## Slide 16
[ M a t e r i a l ]
mat[1] H 2 O 1
[ S u r f a c e ]
10 so 10.
[ C e l l ]
100 1 -1.0 -10
101 -1 10
lec01.inp
H : O = 2 : 1
⇒ H2O（water）
Define materials
H 2 O 1 (Positive number: Atomic ratio)
H -2/18 O -16/18 (Negative number: mass ratio)
Several ways to mix elements
Written in the order of material number, (atom & composition)…
Geometry (General definition)
*When elements are specified without mass number, natural isotopic composition is assumed. Following formats are available to specify the mass number.
Element symbol with mass number (e.g., 1H, 16O)
Formula Z*1000+A (e.g., 1001, 8016)
Notes: 物質を満たす1

## Slide 17: Define surfaces
[ M a t e r i a l ]
mat[1] H 2 O 1
[ S u r f a c e ]
10 so 10.
[ C e l l ]
100 1 -1. -10
101 -1 10
lec01.inp
surface of sphere (so) centered at the origin of the XYZ coordinate system with a radius of 10 cm
In the order of surface number, shape, parameters
Parameters are in units of “cm”
Various types of surfaces are available in PHITS
so, sx, sy, sz, s (Sphere)
px, py, pz (Plane)
cx, cy, cz (Cylinder)
rpp (Rectangular Parallelepiped)
etc. (see Manual 5.5)
Geometry (General definition)
Notes: 球の骨組み

## Slide 18: Define cells
[ M a t e r i a l ]
mat[1] H 2 O 1
[ S u r f a c e ]
10 so 10.
[ C e l l ]
100 1 -1.0 -10
101 -1 10
lec01.inp
100: Cell number
1 : Material number
-1. : Material density
= 1.0 g/cm3
>0 ⇒ atom density in units 1024 atoms/cm3 <0 ⇒ mass density in units of g/cm3
-10 : Inside surface 10
101: Cell number
-1 : Outer void
(density is not necessary)
10 : Outside surface 10
In the order of cell number, material number, density, surface numbers
Geometry (General definition)
Notes: 球の骨組み

## Slide 19: Confirmation of your geometry
lec01.inp
[ P a r a m e t e r s ]
icntl = 8
file(1) = c:/phits
file(6) = phits.out
track_xz.eps
Set 8
when you confirm
the geometry
Procedure to confirm your geometry
Geometry (General definition)
Change “icntl” parameter in the [Parameters] section.
Execute PHITS
See an eps file“track_xz.eps”
Confirm the geometry of lec01.inp.
Notes: ここまで。
領域の二重定義でエラーが出るはずです。

## Slide 20: Exercise 1
[ M a t e r i a l ]
mat[1] H 2 O 1
[ S u r f a c e ]
10 so 10.
[ C e l l ]
100 1 -1.0 -10
101 -1 10
Change the radius of the sphere to 20 cm.
lec01.inp
Geometry (General definition)
Notes: 課題[Surface]セクション
半径5cmの球を作ってみよう。

## Slide 21: Answers 1
Change the radius of the sphere to 20 cm.
lec01.inp
Geometry (General definition)
[ M a t e r i a l ]
mat[1] H 2 O 1
[ S u r f a c e ]
10 so 20.
[ C e l l ]
100 1 -1.0 -10
101 -1 10
track_xz.eps
Is the radius of the sphere 20 cm?
Notes: 課題[Surface]セクション
半径5cmの球を作ってみよう。

## Slide 22: Error message from input file
Geometry (General definition)
22
lec01.inp
[ M a t e r i a l ]
mat[1] H 2 O 1
[ S u r f a c e ]
10 so 20.
[ C e l l ]
100 1 -1.0 -10
101 -1 10
The line number where the mistake was made and its contents are displayed. It may be output to phits.out.
Check contents of the corresponding line number and correct the input file.

## Slide 23: About Input File
Every lecture of PHITS tutorial has a lot of exercises, but only one (or a few) input files are included in each folder.
If you would like to skip some exercises, you can use the input files in “input/” folder, such as lec01-2.inp. For example, if you would like to try the exercise 3, use “lec01-3.inp” in the “input/” folder. “lec01-3.inp” includes all the revisions that have been done in the exercises 1 and 2.
Geometry (General definition)

## Slide 24: Definition of a new surface
Define a spherical surface whose radius is 5 cm and center is at the origin of the XYZ coordinate system.
“10” in the 1st line of [Surface] section is “surface number”. Use “11” for a new surface.
lec01.inp
Geometry (General definition)
[ M a t e r i a l ]
mat[1] H 2 O 1
[ S u r f a c e ]
10 so 20.
11 so 5.
[ C e l l ]
100 1 -1.0 -10
101 -1 10
Notes: 課題[Cell]セクション
半径5cmの球を作ってみよう。

## Slide 25: Exercise 2
“100” in the 1st line of [Cell] section is “cell number”. Use “102” for a new cell.
lec01.inp
Geometry (General definition)
Add a spherical water cell with 5 cm radius to the system.
[ M a t e r i a l ]
mat[1] H 2 O 1
[ S u r f a c e ]
10 so 20.
11 so 5.
[ C e l l ]
100 1 -1.0 -10
101 -1 10
102 *** *** ***
Notes: 課題[Cell]セクション
半径5cmの球を作ってみよう。

## Slide 26: Answer 2
Geometry (General definition)
Add a spherical water cell with 5 cm radius to the system.
lec01.inp
[ M a t e r i a l ]
mat[1] H 2 O 1
[ S u r f a c e ]
10 so 20.
11 so 5.
[ C e l l ]
100 1 -1.0 -10
101 -1 10
102 1 -1.0 -11
Part of cell 100 overlaps cell 102.
⇒ Overlapped region!!
PHITS always identifies the region in which the particle is crossing, so PHITS gets confused when one location is doubly defined.
(geometry error file: track_xz_geo.out)
track_xz.eps
Overlapped region is painted in black.
Notes: 課題[Cell]セクション
半径5cmの球を作ってみよう。

## Slide 27: Geometry error file
Geometry (General definition)
When a geometry error occurs, PHITS outputs an error file (*_geo.out) to provide detailed information on the error.
track_xz_geo.out
Errors of cell definition in EPS Page No. = 1
Overlapped Cell IDs x, y, z coodinates
(Cells 0 0 indicate undefined region)
100 102 -4.847761E+00 1.234568E-11 -1.211940E+00
100 102 -4.847761E+00 1.234568E-11 -1.009950E+00
100 102 -4.847761E+00 1.234568E-11 -8.079602E-01
・・・ ・・・ ・・・ ・・・
Cell numbers. Error is observed there.
x, y, z coordinates of where the geometry error occurs.
Even if only one error occurs, many lines may show up.
Notes: 未定義⇔二重定義 おおよそ対をなす言葉。

## Slide 28: Geometry error (undefined region)
Geometry is defined in an infinite space, but every single point must be filled with certain material (or defined as void).
Geometry (General definition)
Undefined region is painted in purple.
(If undefined region is present, the other region does not appear sometimes.)
Notes: 未定義⇔二重定義 おおよそ対をなす言葉。

## Slide 29
General Description
Geometry
Source
Summary and Homework
Contents
Table of Contents
General definition
How to define cells
Definitions of boxes and cylinders
How to add materials
Geometry drawing software
Notes: 「実習」 前の基本的な話から

## Slide 30
Cells are defined by surfaces using “plus and minus signs” and “Boolean operators”.
Outside and inside of the surface are defined by putting plus and minus signs, respectively, before the surface number.
+11
(outside the surface 11)
Geometry
-11
(inside the surface 11)
AND
blank intersection operator
OR
: union operator
NOT # complement operator
How to define cells
the surface number 11
Boolean operators

## Slide 31: Boolean operator （AND）
[ M a t e r i a l ]
mat[1] H 2 O 1
[ S u r f a c e ]
10 so 20.
11 so 5.
[ C e l l ]
100 1 -1.0 -10 11
101 -1 10
102 1 -1.0 -11
lec01.inp
To define a cell inside or outside of two surfaces, connect the two numbers with a “blank” (AND).
Geometry
track_xz.eps
True answer of the 2nd exercise.
Inside of “10”and outside of “11”
Add ‘+11’ to the definition of the cell 100.
(+ is omissible.)
Notes: ブール代数（積）の表現

## Slide 32
[ C e l l ]
100 1 -1.0 -10 #102
101 -1 10
102 1 -1.0 -11
Geometry
lec01.inp
[ C e l l ]
100 1 -1.0 -10 11
101 -1 10
102 1 -1.0 -11
Exclude the cell number 102 from the inside of the surface 10.
＊Cells are usually defined by using surface numbers, but # must be followed by a cell number.
Define with #.
Boolean operator （NOT）
Use NOT (“#”) to exclude a region.
equivalent
** Use surface numbers inside “()”. This will be explained later.
Notes: ブール代数（否定）の表現

## Slide 33: Extension of virtual space
Geometry
lec01.inp
3D virtual space should be large enough to contain all the geometrical components.
[ M a t e r i a l ]
mat[1] H 2 O 1
[ S u r f a c e ]
10 so 500.
11 so 5.
[ C e l l ]
100 1 -1.0 -10 #102
101 -1 10
102 1 -1.0 -11
track_xz.eps
Change 20 cm to 500 cm.

## Slide 34: Exercise 3
track_xz.eps
lec01.inp
[ M a t e r i a l ]
mat[1] H 2 O 1
[ S u r f a c e ]
10 so 500.
11 so 5.
12 sz 11. 5.
[ C e l l ]
100 1 -1.0 -10 #102 #103
101 -1 10
102 1 -1.0 -11
103 1 -1.0 -12
sphere centered at (0, 0, 11) in the XYZ coordinates with a radius of 5 cm
Geometry
Where is cell “103?”
Notes: 課題[Surface]セクション
半径5cmの球をもう1つ追加してみよう。

## Slide 35: Answer 3
track_xz.eps
lec01.inp
[ M a t e r i a l ]
mat[1] H 2 O 1
[ S u r f a c e ]
10 so 500.
11 so 5.
12 sz 11. 5.
[ C e l l ]
100 1 -1.0 -10 #102 #103
101 -1 10
102 1 -1.0 -11
103 1 -1.0 -12
Geometry
Where is cell “103?”
Spheres are defined with sx, sy, sz.
Universal expression s is used with the XYZ coordinates of its center and its radius.
Notes: この他に、sx, (sy,) sz が使用できます。
（汎用表現はsでXYZ座標と半径の数値入力が必要となります。）
数値を変えることで中心座標と半径を変えることができます。

## Slide 36: Exercise 4
[ S u r f a c e ]
10 so 500.
11 so 5.
12 sz 8. 5.
[ C e l l ]
100 1 -1.0 -10 #102 #103
101 -1 10
102 1 -1.0 -11
103 1 -1.0 -12
lec01.inp
Expected result
track_xz.eps
An overlap of the two spheres causes the geometry error (overlapped region).
← Let’s exclude this overlap region from cells 102 and 103, and create a new cell 104
Change the center of this sphere
Geometry
Correct a geometry error.
Notes: 球が重なる場合

## Slide 37: Answer 4
[ S u r f a c e ]
10 so 500.
11 so 5.
12 sz 8. 5.
[ C e l l ]
100 1 -1.0 -10 #102 #103 #104
101 -1 10
102 1 -1.0 -11 12
103 1 -1.0 -12 11
104 1 -1.0 -11 -12
lec01.inp
track_xz.eps
Geometry
Correct a geometry error.
An example of the answers
Notes: 球が重なる場合

## Slide 38: Boolean operator （OR）
[ C e l l ]
100 1 -1.0 -10 #102 #103 #104
101 -1 10
102 1 -1.0 -11 12
103 1 -1.0 -12 11
104 1 -1.0 -11 -12
lec01.inp
[ C e l l ]
100 1 -1.0 -10 #(-11 : -12)
101 -1 10
102 1 -1.0 -11 12
103 1 -1.0 -12 11
104 1 -1.0 -11 -12
Boolean operator “OR” is expressed by “:”.
equivalent
Geometry (Boolean Operator)
*You have to use surface numbers inside “#()”.
To define a sum of two regions as a cell, connect the two numbers with “:” (OR) sign.
Notes: ブール代数（和）の表現

## Slide 39: A bad example of using unnecessary #’s
input/onion.inp
[ M a t e r i a l ]
mat[1] H 2 O 1
[ S u r f a c e ]
11 so 5.
12 so 10.
13 so 15.
14 so 20.
15 so 25.
[ C e l l ]
101 1 -1. -11
102 1 -1. -12 #101
103 1 -1. -13 #101 #102
104 1 -1. -14 #101 #102 #103
105 1 -1. -15 #101 #102 #103 #104
106 -1 15
[ M a t e r i a l ]
mat[1] H 2 O 1
[ S u r f a c e ]
11 so 5.
12 so 10.
13 so 15.
14 so 20.
15 so 25.
[ C e l l ]
101 1 -1. -11
102 1 -1. 11 -12
103 1 -1. 12 -13
104 1 -1. 13 -14
105 1 -1. 14 -15
106 -1 15
Geometry (Boolean Operator)
Onion geometry
NOT(#) is convenient, but too many #’s can cause slow tracking.
Think twice if the geometry can be defined by simpler expressions using “AND” and “OR”.
Notes: ミルフィーユ（たまねぎ）体系
コード内では、セル番号の否定はすべて展開されています。
空間認識に係る負荷は、計算速度に関係してきますので注意が必要です。

## Slide 40
General Description
Geometry
Source
Summary and Homework
Contents
Table of Contents
General definition
How to define cells
Definitions of boxes and cylinders
How to add materials
Geometry drawing software
Notes: 「実習」 前の基本的な話から

## Slide 41: How to make a box
Geometry
Boxes can be defined using rpp (rectangular parallelepiped)
X
Y
Z
[ S u r f a c e ]
・
・
・
13 rpp xmin xmax ymin ymax zmin zmax
xmin
xmax
ymax
ymin
zmin
zmax
Set the lower and upper boundaries of x, y, z coordinates to define boxes.
*rpp is defined in the [surface] section, because rpp corresponds to 6 surfaces of the box.
Notes: 《休憩はさむ》
直方体を作る。
XYZ座標系はある意味固定されているものなので、
空間をぶった切る“平面”の組み合わせで直方体を作ります。

## Slide 42
[ S u r f a c e ]
10 so 500.
11 so 5.
12 sz 8. 5.
13 rpp *** *** *** *** *** ***
[ C e l l ]
100 1 -1.0 -10 #102 #103 #104 ***
101 -1 10
102 1 -1.0 -11 12
103 1 -1.0 -12 11
104 1 -1.0 -11 -12
105 1 -1.0 ***
Geometry
lec01.inp
Let’s define a 10-cm cube centered at (0, 0, -11) using rpp.
Set xmin = ymin = -5.0 cm, and xmax = ymax = 5.0 cm
Set zmin = -16.0 cm, and zmax = -6.0 cm
Define the inside of the surface specified by rpp as a cell using a symbol -(minus).
Exercise 5
Let’s execute PHITS and see the result to confirm whether a cube is correctly defined or not.

## Slide 43
Geometry
Answer 5
track_xz.eps
[ S u r f a c e ]
10 so 500.
11 so 5.
12 sz 8. 5.
13 rpp -5. 5. -5. 5. -16. -6.
[ C e l l ]
100 1 -1.0 -10 #102 #103 #104 #105
101 -1 10
102 1 -1.0 -11 12
103 1 -1.0 -12 11
104 1 -1.0 -11 -12
105 1 -1.0 -13
lec01.inp
Let’s define a 10cm cube centered at (0, 0, -11) using rpp.

## Slide 44
[ C e l l ]
100 1 -1.0 -10 #102 #103 #104 #105
101 -1 10
102 1 -1.0 -11 12 -14
103 1 -1.0 -12 11
104 1 -1.0 -11 -12
105 1 -1.0 -13
[ S u r f a c e ]
10 so 500.
11 so 5.
12 sz 8. 5.
13 rpp -5. 5. -5. 5. -16. -6.
14 px 3.0
ｐｘ：plane perpendicular to X-axis
Geometry
lec01.inp
x
y
z
3
ｐｘ 3.0
Let’s add red texts and then execute PHITS.
Cells divided by a plane
X axis
X=x0
＋side
－side
To distinguish the two regions divided by a plane, use symbols “+” or “-”.

## Slide 45
Geometry
lec01.inp
track_xz.eps
Cell 102: inside of the surface 11 “AND” outside of the surface 12 “AND” negative region of the surface 14.
(The positive region of the surface 14 in the sphere with the 5-cm radius is cut.)
py and pz are also available.
*Be careful of the meaning of plus and minus when you use planes.
Cells divided by a plane
[ C e l l ]
100 1 -1.0 -10 #102 #103 #104 #105
101 -1 10
102 1 -1.0 -11 12 -14
103 1 -1.0 -12 11
104 1 -1.0 -11 -12
105 1 -1.0 -13
[ S u r f a c e ]
10 so 500.
11 so 5.
12 sz 8. 5.
13 rpp -5. 5. -5. 5. -16. -6.
14 px 3.0
ｐｘ：Plane perpendicular to X-axis

## Slide 46: How to make a cylinder
A cylinder is defined using an infinite cylindrical tube and two planes
Geometry
Notes: 円柱を作る。
XYZ座標系はある意味固定されているものなので、
円柱と、空間をぶった切る“平面”の組み合わせで円柱を作ります。

## Slide 47
[ C e l l ]
100 1 -1.0 -10 #102 #103 #104 #105 ***
101 -1 10
102 1 -1.0 -11 12 -14 ***
103 1 -1.0 -12 11 ***
104 1 -1.0 -11 -12 ***
105 1 -1.0 -13 ***
106 1 -1.0 *** *** ***
Geometry
lec01.inp
Add red texts in the [surface] and [cell] sections.
The cell 106 overlaps the cells 100, 102, 103, 104 and 105.
[ S u r f a c e ]
10 so 500.
11 so 5.
12 sz 8. 5.
13 rpp -5. 5. -5. 5. -16. -6.
14 px 3.0
15 cz 1.
16 pz -19.
17 pz 19.
Exercise 6
Let’s define a cylinder.
The inside and outside correspond to “-” and “+” symbols, respectively.
Let’s execute PHITS and see the result to confirm whether a cylinder is correctly defined or not.
New cell should be excluded

## Slide 48
Geometry
track_xz.eps
lec01.inp
[ S u r f a c e ]
10 so 500.
11 so 5.
12 sz 8. 5.
13 rpp -5. 5. -5. 5. -16. -6.
14 px 3.0
15 cz 1.
16 pz -19.
17 pz 19.
cell 107: a cylinder with a radius of 1.0 cm and a height of 38 cm.
Answer 6
Let’s define a cylinder.
[ C e l l ]
100 1 -1.0 -10 #102 #103 #104 #105 #106
101 -1 10
102 1 -1.0 -11 12 -14 #106
103 1 -1.0 -12 11 #106
104 1 -1.0 -11 -12 #106
105 1 -1.0 -13 #106
106 1 -1.0 -15 16 -17

## Slide 49: Rearrange Cell & Surface numbers
[ S u r f a c e ]
999 so 500.
11 so 5.
12 sz 8. 5.
101 px 3.
111 pz -19.
112 pz 19.
201 cz 1.
301 rpp -5. 5. -5. 5. -16. -6.
Geometry
lec01.inp
While you define geometries, it is useful to rearrange the cell and surface numbers according to your rules.
For example,
rearrange the numbers in an ascending order in each px, py, pz.
[ C e l l ]
100 1 -1.0 -999 #102 #103 #104 #105 #106
101 -1 999
102 1 -1.0 -11 12 -101 #106
103 1 -1.0 -12 11 #106
104 1 -1.0 -11 -12 #106
105 1 -1.0 -301 #106
106 1 -1.0 111 -112 -201

## Slide 50
General Description
Geometry
Source
Summary and Homework
Contents
Table of Contents
General definition
How to define cells
Definitions of boxes and cylinders
How to add materials
Geometry drawing software
Notes: 「実習」 前の基本的な話から

## Slide 51: How to add materials
Geometry (How to add material)
gold（density: 19.32 g/cm3）
Au 1
copper（density: 8.93 g/cm3）
Cu 1
air（density: 1.20x10-3 g/cm3）
N 8 O 2
polyethylene（density: 0.9 g/cm3）
C 2 H 4
Add a new material number and define a composition ratio of the material in [material] section.
(Density is given in [cell] section.)
Notes: 体系の数が多くなったので・・・
金（同位体なし）
銅（天然存在比）
空気（我々の世界ではなくてはならないものだが、コンピューターの世界では1物質）⇔真空
ポリエチレン（化学形による比率）←真空0でも良い。

## Slide 52: Exercise 7
[ M a t e r i a l ]
mat[1] H 2 O 1
mat[2] ******
・・・ ・・・ ・・・ ・・・
[ C e l l ]
100 1 -1.0 -10 #102 #103 #104 #105 #106
101 -1 10
102 1 -1.0 -11 12 -14 #106
103 1 -1.0 -12 11 #106
104 1 -1.0 -11 -12 #106
105 1 -1.0 -13 #106
106 1 -1.0 -15 16 -17
Geometry (How to add material)
lec01.inp
*Each material (number) has its own color.
Execute PHITS and see the result.
Change the material of the cell “106”.
Element symbol of copper is Cu. Density of copper is 8.93 g/cm3
Define the material number 2 in [material] section and the material is used in [cell] section.
Notes: 物質を入れ替える。
同番号は同色

## Slide 53: Answer 7
[ M a t e r i a l ]
mat[1] H 2 O 1
mat[2] Cu 1
・・・ ・・・ ・・・ ・・・
[ C e l l ]
100 1 -1.0 -10 #102 #103 #104 #105 #106
101 -1 10
102 1 -1.0 -11 12 -14 #106
103 1 -1.0 -12 11 #106
104 1 -1.0 -11 -12 #106
105 1 -1.0 -13 #106
106 2 -8.93 -15 16 -17
Geometry (How to add material)
lec01.inp
track_xz.eps
Natural isotopic composition is presumed.
Change the material in the cell “106”.
Notes: 物質を入れ替える。
同番号は同色

## Slide 54: How to make void cells
lec01.inp
Material number for void (inner void) = 0
(Material number for outer void = -1)
Skip density definition of void cells!
Geometry (How to add material)
track_xz.eps
[ C e l l ]
100 0 -10 #102 #103 #104 #105 #106
101 -1 10
102 1 -1.0 -11 12 -14 #106
103 1 -1.0 -12 11 #106
104 1 -1.0 -11 -12 #106
105 1 -1.0 -13 #106
106 2 -8.93 -15 16 -17
Define the cell 100 as void,
and then execute PHITS.
Notes: 物質を入れ替える。
同番号は同色

## Slide 55: Change the colors
Geometry (Change material colors)
55
lec01.inp
[ M a t N a m e C o l o r ]
mat name color
1 Water pastelblue
2 Copper darkred
track_xz.eps
You can specify the name and color of each material (number).
Characters are case sensitive only in this section.
You have to specify the color name in small character.
Notice!
Notes: 物質の色を変える。

## Slide 56: Color definition
Definition in Angel
Geometry (Change material colors)

## Slide 57
General Description
Geometry
Source
Summary and Homework
Contents
Table of Contents
General definition
How to define cells
Definitions of boxes and cylinders
How to add materials
Geometry drawing software
Notes: 「実習」 前の基本的な話から

## Slide 58: Confirmation of geometry with PHIG-3D
58
Windows: Right-click the PHITS input file, and select “Send to” -> “PHIG-3D”.
MacOS: Drag and drop the PHITS input file to the PHIG-3D icon in the Dock*
Linux: In the terminal, move to the folder with the PHITS input file (e.g.: phits.inp), and type “phig3d.sh phits.inp”.
PHITS Interactive Geometry Viewer in 3D (PHIG-3D) :
Input geometry visualization software for PHITS
S.Ohnish, SoftwareX, 14, 100681 (2021).
Let’s see the geometry in 3D view by using PHIG-3D.
An example of an output after mouse operation
Details are in the PHIG-3D manual in the folder (phits/phig3d/manual).
*If you get an unidentified developer error, you have to open the icon of PHIG-3D as well as “phits/phig3d/macos-x86_64/phig3d_mac” with pressing “ctrl” key

## Slide 59: Cut of a cross section with an auxiliary plane
59
Geometry (3D plot with PHIG-3D)
Select the setting pane -> Check the X box in the aux plane -> Select + with a radio button -> Click “Draw”
“Setting pane”
“Draw”
The cross section is displayed.
Result of a cutting plane at x=0 cm.
Notes: Cut a geometry with up to three planes. Here a plane is perpendicular to the x, y, and z axes, respectively. A plane is enabled/disabled with its check box. With a radio button, you can select to “cut a plane with a plus side/ cut a plane with a minus side/display a position of a plane without cutting”

## Slide 60: Select cells for visualization
60
Geometry (3D plot with PHIG-3D)
Select the cell pane-> Uncheck the checkbox of cell 102 -> Click “Draw”
“Cell pane”
“Draw”
Cell 102 is not displayed.
Result of a cutting plane at x=0 cm.
Notes: After an input file is read, the list of cells is displayed in the cell pane. We can select cells for visualization in the cell plane.

## Slide 61: Change the colors
61
Geometry (3D plot with PHIG-3D)
Select “Tools-Configuration” in the menu bar -> Select colors of background / materials in the color tab -> Click “OK”.
“Color tab”
*Changing the colors is available with the [ Mat Name Color ] section in PHITS.
Result after changing colors
Notes: The color table in the lower part of this dialog sets the name of materials and another name corresponding to them (name in legend), display scale of legend and their color. These setting parameters correspond to the [Mat Name Color] section in PHITS.

## Slide 62: SuperMC
A free software developed by the FDS team at the Chinese academic of Science (registration required)
Software to convert CAD geometry into several MC code format (MCNP, FLUKA, GEANT4, TORIPOLI & PHITS)
Compatible CAD formats are *.sat, *.sab, *.stp &*.step
SuperMC + PHITS sample (utility\SuperMC)
Instruction only available in Japanese at the moment
https://www.oecd-nea.org/tools/abstract/detail/iaea1437/
To obtain license, utility\SuperMC\license\FirstEmail.txt

## Slide 63
General Description
Geometry
Source
Summary and Homework
Contents
Table of Contents
General definition
How to define cells
Definitions of boxes and cylinders
How to add materials
Geometry drawing software
Notes: 「実習」 前の基本的な話から

## Slide 64: Main components of an input
Source
[Source]
define source
In the PHITS simulation, geometry in 3-dimensional virtual space and information on source particles are essential to tally various quantities of the particles.
⇒ ① Geometry
② Source
③ Tally
Notes: 《休憩はさむ》
次は[Source]セクション（線源）の話です。

## Slide 65: Types of sources
Radio-Isotope (RI) facilities
→ Point isotropic source
Accelerator facilities
→ Pencil or broad beam to certain direction
→ Cone beam source
Radioactive waste and internal exposure
→ Volume isotropic source
Cosmic-ray and external exposure
→ Isotropic irradiation within certain area
Source
Notes: 放射状かビーム状に大きく分類されます。
（放射線の名の由来通り）

## Slide 66: Definition of sources
Shape of source distribution
← spatial distributions
(point, cylindrical, spherical etc.)
Energy of source particle
← mono-energy or having a spectrum
Source particle species
← neutron, photon, proton, heavy-ion etc.
Direction of source particle
← isotropic, directional, cone shape etc.
Source
Notes: 基本的な3要素になります。

## Slide 67: Shape of source particles
lec01.inp
[ S o u r c e ]
s-type = 1
proj = proton
dir = 1.0
r0 = 0.0
z0 = 0.
z1 = 0.
e0 = 150
[ S o u r c e ] section
: definition of sources
s-type: Define source type
= 1 cylindrical shape
What information is required to define a cylinder?
Source

## Slide 68
Source
X,Y coordinates of center position: （x0, y0）
r0: radius of cylinder
（r1: inner radius）
Z0: minimum Z
Z1: maximum Z
Z-axis
Definition of a cylinder source
The default direction of PHITS is +z.

## Slide 69
Source
Cylinder
z0 = z1
e.g.
z0 = 5.0
z1 = 5.0
z0 = z1
r0 = 0.0
Extension of cylinder source
Disk
Point
Z-axis
Z-axis
Z-axis
(Note) Source disk or points should not be set on boundaries of cells

## Slide 70
[ P a r a m e t e r s ]
icntl = 0
file(1) = c:/phits
file(6) = phits.out
Transport
calculation
Source
70
lec01.inp
[ S o u r c e ]
s-type = 1
proj = proton
dir = 1.0
r0 = 0.
z0 = 0.
z1 = 0.
e0 = 150
Point source at the origin (0,0,0)
[ T - T r a c k ]
・・・ ・・・ ・・・ ・・・
t-type = 2
nt = 10
tmin = 0.
tmax = 1.
Output of transport from 0 to 1 nsec, in 0.1 nsec increments.
track_xz.eps has 10 pages
*In GSview, you can switch the pages of *.eps by space and backspace keys
Exercise 8
Execute the transport calculation.
Notes: サンプルインプットの結果

## Slide 71
[ P a r a m e t e r s ]
icntl = 0
file(1) = c:/phits
file(6) = phits.out
Transport
calculation
Source
71
lec01.inp
[ S o u r c e ]
s-type = 1
proj = proton
dir = 1.0
r0 = 0.
z0 = 0.
z1 = 0.
e0 = 150
[ T - T r a c k ]
・・・ ・・・ ・・・ ・・・
t-type = 2
nt = 10
tmin = 0.
tmax = 1.
track_xz.eps
(1 page[0nsec～0.1nsec])
Point source at the origin (0,0,0)
track_xz.eps
(3 page[0.2nsec～0.3nsec])
track_xz.eps
(5 page[0.4nsec～0.5nsec])
Answer 8
Execute the transport calculation.
Output of transport from 0 to 1 nsec, in 0.1 nsec increments.
Notes: サンプルインプットの結果

## Slide 72: Exercise 9
Source
lec01.inp
[ S o u r c e ]
s-type = 1
proj = proton
dir = 1.0
r0 = 0.
z0 = 0.
z1 = 0.
e0 = 150
Make a disk source with a radius of 1 cm.
Notes: 課題[Source]セクション

## Slide 73: Answer 9
Source
lec01.inp
[ S o u r c e ]
s-type = 1
proj = proton
dir = 1.0
r0 = 1.
z0 = 0.
z1 = 0.
e0 = 150
The radius of the beam is 1cm.
Make a disk source with a radius of 1 cm.
track_xz.eps
(1 page[0nsec～0.1nsec])
Notes: 課題[Source]セクション

## Slide 74: Energy distribution of source particles
lec01.inp
[ S o u r c e ]
s-type = 1
proj = proton
dir = 1
r0 = 1.0
z0 = 0.
z1 = 0.
e0 = 150
Mono-energy:
the energy is defined by e0.
Energy spectrum:
the distribution is defined by e-type subsection.
(For details;
lecture\advanced\sourceA
or Manual 5.3.19)
In units of “MeV/nucleon”
(MeV per nucleons)
Source

## Slide 75: Source particle species
lec01.inp
[ S o u r c e ]
s-type = 1
proj = proton
dir = 1
r0 = 1.0
z0 = 0.
z1 = 0.
e0 = 150
proj: particle species
Both ‘symbol’ and ‘kf-code’ are available.
Source
To use radioisotope sources, specify the particle species, such as ‘photon’.
nucleus is specified by
(mass number)+(element symbol)
e.g., 12C

## Slide 76: Exercise 10
Source
lec01.inp
[ S o u r c e ]
s-type = 1
proj = proton
dir = 1.0
r0 = 1.
z0 = 0.
z1 = 0.
e0 = 150
Define a neutron source at 100 MeV.
Notes: 課題[Source]セクション

## Slide 77: Answer 10
track_xz.eps
(10 page[0.9nsec～1nsec])
Source
lec01.inp
[ S o u r c e ]
s-type = 1
proj = neutron
dir = 1.0
r0 = 1.
z0 = 0.
z1 = 0.
e0 = 100
Neutrons penetrate materials unlike protons.
Define a neutron source at 100 MeV.
Notes: 課題[Source]セクション

## Slide 78: Direction of source particles
Source
dir: cosine of the angle between the pointing direction and the z-axis
e.g. q =0 (deg): dir=1.0.
q =90 (deg): dir=0.0
Special: dir=all; isotropic source
The direction is defined in the spherical coordinate system.
Z-axis is the default direction in PHITS.
Defined by polar angle (dir), azimuthal angle (phi), and beam spread (dom).
dir = 1.0
dir = cosq
Z-axis
q (deg)

## Slide 79
Source
phi (f in units of degrees): counterclockwise angle between the +x-axis and the projection onto the xy-plane
e.g. the direction tilted by 45 degrees from the +x-axis on the xy-plane:
dir=0.0, phi=45
Direction of source particles
Z-axis
f (deg)
Y-axis
X-axis
Defined by polar angle (dir), azimuthal angle (phi), and beam spread (dom).
The direction is defined in the spherical coordinate system.
Z-axis is the default direction in PHITS.

## Slide 80
Source
dom: solid angle W (degree)
e.g. a beam spread of 30 degrees: dom=30
W (deg)
Direction of source particles
Defined by polar angle (dir), azimuthal angle (phi), and beam spread (dom).
The direction is defined in the spherical coordinate system.
Z-axis is the default direction in PHITS.

## Slide 81: Source direction and parameters
Source
Z-axis
f =phi
Y-axis
X-axis
q
cosq =dir
W =dom
Relation of dir, phi, and dom in the spherical coordinate system

## Slide 82: Exercise 11
Source
lec01.inp
[ S o u r c e ]
s-type = 1
proj = neutron
dir = 1.0
r0 = 1.
z0 = 0.
z1 = 0.
e0 = 100
Define an isotropic point source at the XYZ coordinate （0, 0, 10）.
When s-type=1, you can set an isotropic source by setting dir=all.
Notes: 課題[Source]セクション

## Slide 83: Answer 11
Source
lec01.inp
[ S o u r c e ]
s-type = 1
proj = neutron
dir = all
r0 = 0.
z0 = 10.
z1 = 10.
e0 = 100
When s-type=1, you can set a isotropic source by setting dir=all.
Let’s set a point isotropic source at the XYZ coordinate （0, 0, 10）.
track_xz.eps
(1 page[0nsec～0.1nsec])
Notes: 課題[Source]セクション

## Slide 84
General Description
Geometry
Source
Summary and Homework
Contents
Table of Contents
General definition
How to define cells
Definitions of boxes and cylinders
How to add materials
Geometry drawing software
Notes: 「実習」 前の基本的な話から

## Slide 85: Summary
Summary
The main components of a PHITS input file are “Geometry”, “Source” and “Tally”
“Geometry” is defined by [material], [surface] and [cell] sections, and you can define various 3D geometrical components based on the GG concept
“Source” is defined by shape, species, energy and direction of the particles
“Tally” is used to calculate the quantities in PHITS radiation transport calculation.
You will learn more about “Tally” in phits-lec02-en.ppt
Notes: 《休憩はさむ》
まとめ

## Slide 86: Homework #1 (Geometry)
Homework
Delete cell 1 (Aluminum sphere)
Make a cylinder with a 10 cm radius and a 50 cm height (starting at z = 0 cm) filled with water. The outside of the cylinder is void (do not change cell 100 & 101)
Confirm the geometry (icntl = 8)
X-axis
Y-axis
Z-axis
R-axis
3D space
Start with “Phits\lecture\basic\homework\homework1.inp”
cz
cz
pz
pz
Notes: 宿題（3次元体系）

## Slide 87: Homework (source)
X-axis
Y-axis
Z-axis
R-axis
3D space
cz
cz
pz
pz
Set a proton beam at 290 MeV/u with a 2.5 cm radius, incident from the bottom of the cylinder
Execute the transport calculation (icntl = 0)
source
Homework
Notes: 宿題（線源）

## Slide 88
Example Answer
Homework
Sum of the proton and neutron trajectories
xz_track.eps