## Slide 1
How to stop a, b, g-rays and neutrons?
title
Sep. 2020 revised
Notes: PHITS講習会 入門実習

## Slide 2
α particles can be stopped by a piece of paper
β rays can be stopped by an aluminum plate
γ rays can be stopped by a lead block
neutrons can penetrate all of these materials
Contents
Purpose of this Exercise
It is generally said that …
Let’s check whether they are correct or not, using PHITS!
Notes: 「実習」 前の基本的な話から

## Slide 3: Check Range.inp
*Error bar is depicted when epsout = 2
Calculation Condition
track.eps
Photons with an energy distribution (r = 0.01cm)
Cylindrical Al shielding (t = 0.1cm, r = 5cm) & Void
[t-track] for visualizing particle trajectories
[t-cross] for calculating particle fluences behind the shielding
(Error bars are plotted by setting epsout = 2)
cross.eps*
Geometry
Incident particles：
Geometry：
Tally：
Photon
Al
Void

## Slide 4: Source with Energy Distribution
Energy distribution is defined by e-type subsection.
[ S o u r c e ]
s-type = 1
proj = photon
r0 = 0.0100
x0 = 0.0000
y0 = 0.0000
z0 = -20.000
z1 = -20.000
dir = 1.0000
e-type = 21
ne = 3
$ E_low Flux(/MeV)
0.0 1.0
1.0 3.0
2.0 1.0
3.0
e-type = 21: number of energy bins (ne)
lower boundary of each bin (MeV)
Relative fluence in each energy bin (/MeV)
Lower boundary of each energy bin (ne+1)
Relative fluence in each bin (/MeV)
1 : 3 : 1
See manual or lecture\advanced\sourceA for more detail

## Slide 5
Procedure
Change the source to β-rays
Change the thickness of the Al shielding
Change the tallied region
Change the source to α-rays
Change the target to a piece of paper
Change the source to γ-rays, and the target to a lead block
Find an appropriate thickness of the lead block
Reduce the statistical uncertainty
Change the source to neutrons
Find an appropriate shielding material for neutrons
The input file for each procedure are prepared as “range*.inp”
Procedure for this exercise

## Slide 6: Step 1：Change Source
Step 1
1. Change energy distribution according to Table 1 → Check cross.eps
[ S o u r c e ]
s-type = 1
proj = photon
r0 = 0.0100
x0 = 0.0000
y0 = 0.0000
z0 = -20.000
z1 = -20.000
dir = 1.0000
e-type = 21
ne = 3
$ E_low Flux(/MeV)
0.0 1.0
1.0 3.0
2.0 1.0
3.0
Energy range | Relative Fluence (/MeV)
0 ～ 0.5 MeV | 2.0
0.5 ～ 1.0 MeV | 1.0
1.0 ～ 1.5 MeV | 0.5
Table 1 Relative fluence of β-rays
cross.eps after step1
track.eps after step2
(2nd page)
Change parameters in red
2. Change particle to electron (proj) → Check track.eps

## Slide 7: Step 2: Change the Thickness
Step 2
Thickness of target is defined as the variable c1
Find an appropriate thickness of the Al plate, which can fully stop electrons (check by a 1-mm step)
Electron fluence (track.eps, 2nd page)
3 mm is thick enough!
[ S u r f a c e ]
set: c1[0.1] $ Thickness of Target (cm)
1 pz 0.0
2 pz c1
3 pz 50.0
11 cz 5.0
999 so 100.0

## Slide 8: Step 3：Change Tally Region
Step 3
Target thickness (c1) should be 0.3 cm
Tally from -c1 to +c1 cm for X&Y directions
Tally from 0 to c1*2 cm for Z direction
[ T - T r a c k ]
title = Track in
mesh = xyz
x-type = 2
xmin = -1.5
xmax = 1.5
nx = 50
y-type = 2
ymin = -1.5
ymax = 1.5
ny = 1
z-type = 2
zmin = 0.0
zmax = 3.0
nz = 90
Let’s see the fluence distribution inside the target in more detail!
Electron fluence
Stopped close to the distal edge
Photon fluence
Penetrated
-c1
c1
-c1
c1
c1*2

## Slide 9
Step 3
Particle fluence behind the target（cross.eps）
Photons with energies from 10 keV to 500 keV escape
Integrated value?
You can find the integrated fluence per source at ”# sum over” at the 70 line of cross.out
0.024 photons/incident electron escape from the aluminum plate
An aluminum plate, which is thick enough to stop β-ray, is not thick enough to stop secondary photons!
Check Energy Spectrum
photon... electron
…
# sum over 2.4091E-02 0.0000E+00

## Slide 10: Step 4: How about α particles?
10
*See lecture\advanced\SourceA for more detail
Fluence of α particles
(3rd page of track.eps)
Change the source to α particles emitted from 210Po decay
Particle type is defined by “proj” (α particle is “alpha”)
Use RI source function (e-type = 28)*
Replace # of energy bins (ne) by # of Isotopes (ni)
Define RI & its activity in Bq (e.g. Po-210 1.0)
[ S o u r c e ]
s-type = 1
proj = electron
r0 = 0.0100
x0 = 0.0000
y0 = 0.0000
z0 = -20.000
z1 = -20.000
dir = 1.0000
e-type = 21
ne = 3
$ E_low Flux(/MeV)
0.0 2.0
0.5 1.0
1.0 0.5
1.5
e-type = 28
ni = 1
Po-210 1.0
alpha

## Slide 11: Step 5: Change Geometry
[ M a t e r i a l ]
MAT[ 1 ] # Aluminum
27Al 1.0
[ C e l l ]
1 1 -2.7 1 -2 -11 $ Target
2 0 2 -3 -11 $ Void
98 0 #1 #2 -999 $ Void
99 -1 999 $ Outer region
[ S u r f a c e ]
set: c1[ 0.3 ] $ Thickness of Target (cm)
1 pz 0.0
2 pz c1
3 pz 50.0
11 cz 5.0
999 so 100.0
C 6.0 H 10.0 O 5.0
-0.82
0.01
Step 5
Fluence of α particle
Stop at 0.005 cm in paper
No secondary particles are generated
Change the target to a piece of paper (C6H10O5)n
Assume density = 0.82 g/cm3 & thickness = 0.01 cm

## Slide 12: Step 6: How about γ-rays?
Step 6
Change the source to g-rays at 0.662 MeV
Change the target to a 1 cm lead (Pb) block (11.34 g/cm3)
Photon fluence
Target thickness is not enough
Energy spectra behind the target
Most of source photons penetrate the target without reactions
Use mono-energetic source (e0) instead of RI source (e-type=28)

## Slide 13: Step 7: Find an appropriate thickness
13
Step 7
Photon fluence for
the 4.4-cm lead target case
Change the target thickness to decrease the direct penetration rate of photons down to 0.01
Check the 45th line (0.6 MeV < E < 0.7 MeV) in cross.out
Energy spectrum
Penetration rate = 0.009
Statistically insignificant!

## Slide 14: Step 8: Consider Statistical Uncertainty
Step 8
Estimate a statistically-significant shielding thickness that has a penetration rate < 0.01, by changing maxcas, maxbch, batch.out, istdev etc.
0.00959 4.06% → The penetration rate is below 0.01 with statistical significance
Elow(MeV) Ehigh(MeV) Photon r.err
2.0000E-01 3.0000E-01 0.0000E+00 0.0000
3.0000E-01 4.0000E-01 0.0000E+00 0.0000
4.0000E-01 5.0000E-01 1.5326E-03 0.7118
5.0000E-01 6.0000E-01 1.1820E-03 0.7078
6.0000E-01 7.0000E-01 9.1494E-03 0.2348
See the 45th line in cross.out
Statistical uncertainty is too large (~23%)
2.0000E-01 3.0000E-01 8.2373E-05 0.5927
3.0000E-01 4.0000E-01 8.0646E-04 0.2499
4.0000E-01 5.0000E-01 1.4322E-03 0.1340
5.0000E-01 6.0000E-01 2.9153E-03 0.0810
6.0000E-01 7.0000E-01 9.5912E-03 0.0406
Thickness = 4.4 cm，maxcas = 2000, maxbch = 1
Thickness = 4.2 cm，maxcas = 2000, maxbch =32

## Slide 15: Step 9: How about neutrons?
Step 9
Change the source to neutron at 1.0 MeV
Set “maxbch = 3”
Neutron fluence
Penetrate!
Energy spectra
80% of neutrons penetrate the
target without reactions

## Slide 16: Step 10: Shielding material for neutrons
Step 10
C (1.77 g/cm3)
ca. 27 cm
Change the target material and thickness in order to decrease the penetration rate of neutrons down to 0.01 (see ”# sum over”@ the 70th line)
Try various materials for the target. Find out an appropriate shielding material for neutrons
H2O (1.0 g/cm3)
ca. 18 cm
Light nuclei (e.g. hydrogen) are suitable for neutron shielding
Al (2.7 g/cm3)
ca. 40 cm

## Slide 17
Common sense on the shielding profiles of α, β, γ rays and neutrons has been confirmed by PHITS simulations.
PHITS is useful for particle transport simulation in a mixed radiation field owing to its applicability to various radiation types.
Summary
Summary

## Slide 18
Homework
Let’s design a shielding for high-energy neutrons (100 MeV)
Index for the effectiveness of shielding is not the fluence but the effective dose
Find the thinnest shielding that can reduce the doses by 2 order of magnitude
Combine 2 materials for the shielding
Homework (challenge!)
Hints
Use [t-track] in “h10multiplier.inp” in the recommendation settings
See the histogram of the dose by changing the axis from “xz” to “z”
Change “nx” parameter to 1 to simplify the files
Low-energy neutrons are effectively shielded by light nuclei, while high-energy neutrons are shielded by intermediate-mass nuclei

## Slide 19
Homework
Example of Answer（answer1.inp）
Let’s Think
How much of the total dose is contributed by photon?
Why 2-layer shielding is more effective than a mono-layer one?
What happens when the order of the 2 layers is inverted?
2-layer shielding that consists of 80 cm iron and 25 cm concrete
Iron
Concrete
Air