## Slide 1: PHITS
PHITS Tutorial
PHITS simulation using DICOM
Multi-Purpose Particle and Heavy Ion Transport code System
Title
1
Feb. 2018 revised

## Slide 2
Table of Contents
2
Contents
How to use DICOM2PHITS
Application using DICOM2PHITS
How to use PHITS2DICOM
Notes: PHITS講習会 入門実習

## Slide 3: DICOM format (Binary)
3
① Header (Information on time, voxel size etc.)
② CT values（1,1→2,1→3,1→…→nx-1, ny → nx, ny）
Data for 1 slice （sample001.dcm）
Several files are contained in one folder to represent an object
cross sectional view
3D view
It is necessary to convert from DICOM to PHITS-input format
(CT value, binary) (Universe number, text)
What is DICOM

## Slide 4: DICOM2PHITS
DICOM2PHITS input Signature for a DICOM2PHITS input
"data/HumanVoxelTable.data" Conversion table
"DICOM/" DICOM files are automatically identified in this directory
"PHITSinputs/" Directory for PHITS inputs to be created
1 20 Slices to be used (1<=z<=20)
1 512 1 512 Clipping (1<=x<=512, 1<=y<=512)
8 8 1 Coarse graining (Average on 4 times 4 voxels in x and y direction)
0 Origin: 0:Voxel center 1:DICOM center
2 PHITS parameter: 1:Photon therapy 2:Particle therapy
4
Convert from Dicom data to PHITS input format (voxel phantom)
Relation between CT value and material density is defined in data/HumanVoxelTable.data
1. Make an input file for DICOM2PHITS （dicom2phits.inp） Details given in README
2. Execute
Windows: Drag dicom2phits.inp and drop into dicom2phits.bat
Mac: Double click dicom2phits.command and type dicom2phits.inp + enter
DICOM2PHITS HowTo

## Slide 5: Outputs of DICOM2PHITS
5
A sample input (phits.inp) for PHITS is created
in the specified directory (work/PHITSinput/)
In addition, the following include files are created
・material.inp : A file containing material info
・universe.inp : A file specifies universe for each material
・voxel.inp : A file containing voxel data converted to PHITS format
・libpath.inp : A file specifying paths for nuclear and photon data library
“libpath.inp” is created only when it dose not exist. Modification is required to fit the path of file(1) following your environment but once the file is created and modified in the specified folder no need of the modification at the second and later time.
DICOM2PHITS outputs
file(1) = c:/phits
libpath.inp
Modification is not necessary for default Windows installation

## Slide 6: Generated Input File
6
phits.inp
file=phits.inp
[ Parameters ]
...
[ S u r f a c e ]
set: c81[ 64] $ number of x pixel
set: c82[ 64] $ number of y pixel
set: c83[ 20] $ number of z pixel
set: c84[ 0.37600] $ unit voxel x
set: c85[ 0.37600] $ unit voxel y
set: c86[ 0.50000] $ unit voxel z
…
[Surface]
$ Unit voxel
5000 rpp -c87 -c87+c84 -c88
-c88+c85 -c89 -c89+c86
$ Outer region
99 so 500
$ Main Space
97 rpp -c87+c90 c87-c90 -c88+c90
c88-c90 -c89+c90 c89-c90
98 500 rpp -c87+c90 c87-c90
-c88+c90 c88-c90 -c89+c90 c89-c90
Always 1st line. Necessary for
using “infl” command
[ C e l l ]
$ Material universe
infl:{universe.inp}
$ Voxel universe
5000 0 -5000 lat=1 u=5000
fill= 0: 63 0: 63 0: 19
infl: { voxel.inp }
$ Main space
97 0 -97 trcl=500 fill=5000
98 0 -99 #97 $ Void
99 -1 99 $ Outer region
Include file command
Voxel data file generated as is specified in DICOM2PHITS
Center of voxel phantom is set at the origin of the XYZ coordinate
Dicom to PHITS
Size and number of voxels are automatically adjusted
Transform is feasible
Refer to “PHTS Tutorial for making Voxel Phantom” (phits/lecture/advanced/voxel/phits-lec-voxel-jp.ppt) for details

## Slide 7
Conversion table
Table for human voxel based on W. Schneider, Phys. …
24 ! Number of universe di …
-1000.0d0 -1.21e-3 3 ! Lowest CT value, Dens
-950.0d0 -0.26 10 ! Universe 2
-120.0d0 -0.927 8 ! Universe 3
-82.0d0 -0.958 8 ! Universe 4 NOTE: Den …
-52.0d0 -0.985 9 ! Universe 5 [10^…
-22.0d0 -1.012 8 ! Universe 6 [g/…
…
1500.0d0 -1.935 11 ! Universe 24
1600.0d0 ! Highest CT value for…
#1 Air :: Air density is used ! Composition
14N -75.5 ! Element, Ele…
16O -23.2 !
40Ar -1.3 !
#2 Lung :: Lung density is used ! Composition o…
1H -10.3
12C -10.5
14N -3.1
…
e.g. data/HumanVoxelTable.data [Ref. W. Schneider, Phys. Med. Biol. 45(2000)459}
1st line：Comment appearing at execution
2nd line：Number of materials
3rd line：Definition of material 1
Smallest CT value
Density
Number of elements
-1000  material 1 < -950
Largest CT value for the last material
Partition line：starting with #
Composition of material 1
Partition line：starting with #
Ratio: > 0 particle density ratio, <0 weight ratio
Element
< Smallest CT value of material 1 => Show warning msg. and substitute material l
> Largest CT value of the last material => Show warning msg. and substitute the last material
21
Conversion table

## Slide 8
8
icntl = 11
icntl = 8
CT3D.eps
deposit-xy.eps
Geometry check
Geometry check

## Slide 9
9
dicom2phits.inp
DICOM2PHITS input
"data/HumanVoxelTable.data" ! File for conversion of human voxel data
"work/DICOM/" ! DICOM file directory
"work/PHITSinput/" ! Filename for voxel include file
2 19 ! Minimum slice number, Maximum slice number
70 430 90 460 ! Clipping: Nxmin, Nxmax, Nymin, Nymax
8 8 1 ! Coarse graining: Nxc, Nyc, Nzc
1 ! Origin 0:Voxel center 1:DICOM center
2 ! PHITS parameter: 1:PhotonTherapy 2:Particle Therapy
deposit-xy.eps
Change voxelized region
Region specification
[ Transform ]
$ Transform system according to DICOM header
tr500 -12.00770 -12.00775 -117.80000
1.00000 0.00000 0.00000
0.00000 1.00000 0.00000
0.00000 0.00000 1.00000
1
Object position is extracted from DICOM header and the object is transformed in this position for origin option = 1

## Slide 10: Rotation & translation
[transform]
10
n: ID of transformation
O1,O2,O3: Displacement vector
B1～B9: Elements of rotation matrix
M: Parameter to change the equation of the transformation（The case of M=1 is shown here.)
[ T r a n s f o r m ]
Trn O1 O2 O3 B1 B2 B3 B4 B5 B6 B7 B8 B9 M
In the case of M=1,
After making [transform] section, you can use this function by setting trcl=n in [cell], [source], and so on.
+

## Slide 11
11
icntl = 0
Dose calculation
Example of dose calculation
deposit-xy.eps
unit = 2
⇒ MeV/cm3/source
unit = 0
⇒ Gy/source
Proton 100 MeV
[But without using EGS (negs=0) because it takes too long due to many materials]

## Slide 12
Table of Contents
12
Contents
How to use DICOM2PHITS
Application using DICOM2PHITS
How to use PHITS2DICOM
Notes: PHITS講習会 入門実習

## Slide 13: Advanced application
DICOM2PHITS input
"data/HumanVoxelTable.data" ! File for conversion of human voxel data
"work_Kumamoto/DICOM/" ! DICOM file directory
"work_Kumamoto/PHITSinput/" ! Filename for PHITS input
1 148 ! Minimum slice number, Maximum slice number
83 430 150 400 ! Clipping: Nxmin, Nxmax, Nymin, Nymax
8 8 2 ! Coarse graining: Nxc, Nyc, Nzc
1 ! Origin 0:Voxel center 1:DICOM center
2 ! PHITS parameter: 1:PhotonTherapy 2:ParticleTherapy
1. Execute DICOM2PHITS using modified dicom2phits.inp as follows
13
Further application
2. Execute PHITS with icntl=8 using phits.inp at the folder work_Kumamoto/PHITSinput
[But without using EGS (negs=0) because it takes too long due to many materials]
deposit-xy.eps
deposit-xz.eps

## Slide 14: Reduce computational time
14
It converts its input file to binary, and re-reads the binary file
Make binary file of voxel phantom prior to the PHITS execution
Purpose
Procedure
① Insert the following 2 lines in the [Parameters] section
ivoxel = 2 # Convert the “fill” part of lattice to binary and output to file(18)
file(18) = voxel.bin # Output file name for binary voxel phantom
② Execute PHITS → Binary file was successfully generated!!
③ Change “ivoxel = 1”, and comment out “infl” command
ivoxel = 1 # Read the “fill” part of lattice from file(18)
$ infl:{voxel.inp}
Speed up!
Dicom to PHITS
It is better to…
Every time PHITS runs…

## Slide 15
15
Application: Modification of beam profile
[ Transform ]
$ Transform source directing beam along x-axis
tr400 -0.31739 -14.15528 -11.37500
$ Center of radiation field
1.00000 0.00000 0.00000
0.00000 0.00000 -1.00000
0.00000 1.00000 0.00000
1
…
[ Source ]
s-type = 1
$ Create radiation field centered on 0
$ Adjust center of radiation field in trcl=400
x0 = 0.0
y0 = 0.0
z0 = 0.0
z1 = 0.0
r0 = 5.0
dir = 1.0
trcl = 400
…
deposit-xz.eps
icntl = 0
-11.375
-0.31739
5.0
-10.0
Beam position change
How does this change?
5.0
-10.0
Application: Beam modification
x, z: Center of RF -> Voxel center
y: Beam start -> Voxel edge
Beam is transformed into y-direction by Trcl=400

## Slide 16
16
Application: Modification of beam profile
[ Transform ]
$ Transform source directing beam along x-axis
tr400 5.0 -14.15528 -10.0
$ Center of radiation field
1.00000 0.00000 0.00000
0.00000 0.00000 -1.00000
0.00000 1.00000 0.00000
1
…
[ Source ]
s-type = 1
$ Create radiation field centered on 0
$ Adjust center of radiation field in trcl=400
x0 = 0.0
y0 = 0.0
z0 = 0.0
z1 = 0.0
r0 = 5.0
dir = 1.0
trcl = 400
…
deposit-xz.eps
icntl = 0
5.0
-10.0
Circular surface source of radius 5cm
5cm
10cm
10cm
Field shape change
How does this change?
x0 = -5.0
x1 = 5.0
y0 = -5.0
y1 = 5.0
z0 = 0.0
z1 = 0.0
$ r0 = 5.0
dir = 1.0
trcl = 400
Square surface source of 10cm x 10cm
2
Application: Beam modification
Set radiation field in xy plane centering 0

## Slide 17
17
Application: Beam modification
Modification of beam profile
[ Transform ]
$ Transform source directing beam along x-axis
tr400 -0.31739 -14.15528 -11.37500 $ Center of radiation field
…
[ Source ]
s-type = 1
$ Create radiation field centered on 0
$ Adjust center of radiation field in trcl=400
x0 = 0.0
y0 = 0.0
z0 = 0.0
z1 = 0.0
r0 = 5.0
dir = 1.0
trcl = 400
…
Beam is transformed into y-direction by Trcl=400
x, z: Center of RF -> Voxel center
y: Beam start -> Voxel edge
(x,z)=
(-0.31739,-11.37500)
(x,z)=(5.0,-10.0)
Beam position change
deposit-xz.eps
icntl = 0
[ Transform ]
$ Transform source directing beam along x-axis
tr400 5.0 -14.15528 -10.0
$ Center of radiation field
…
[ Source ]
s-type = 1
$ Create radiation field centered on 0
$ Adjust center of radiation field in trcl=400
x0 = 0.0
y0 = 0.0
z0 = 0.0
z1 = 0.0
r0 = 5.0
dir = 1.0
trcl = 400
Set radiation field center for (x, z)
deposit-xz.eps
icntl = 0

## Slide 18
18
Application: Beam modification
Modification of beam profile
[ Transform ]
$ Transform source directing beam along x-axis
tr400 5.0 -14.15528 -10.0
$ Center of radiation field
…
[ Source ]
s-type = 1
$ Create radiation field centered on 0
$ Adjust center of radiation field in trcl=400
x0 = 0.0
y0 = 0.0
z0 = 0.0
z1 = 0.0
r0 = 5.0
dir = 1.0
trcl = 400
…
Circular surface source of radius 5cm
Set radiation field in xy plane centering 0
Cylindrical source
deposit-xz.eps
icntl = 0
[ Transform ]
$ Transform source directing beam along x-axis
tr400 5.0 -14.15528 -10.0
$ Center of radiation field
…
[ Source ]
s-type = 2
$ Create radiation field centered on 0
$ Adjust center of radiation field in trcl=400
x0 = -5.0
x1 = 5.0
y0 = -5.0
y1 = 5.0
z0 = 0.0
z1 = 0.0
dir = 1.0
trcl = 400
Rectangular source
Square surface source of 10cm x 10cm
deposit-xz.eps
icntl = 0
5cm
10cm
10cm
Field size change

## Slide 19
19
icntl = 0
Dose with modified beam
Application: Dose calculation with modified beam
deposit-xy.eps
Beam range is elongated due to low density in lung

## Slide 20: How to Deal with High-Resolution Phantom?
20
High resolution voxel phantom requires numerous memory
Default setting of PHITS is allowed to use memory only less than 640 MByte
e.g.) Whole body voxel phantom (180cm×30cm×50cm) with 1mm3
resolution consists of 270,000,000 voxels, and costs 5.4 GByte
memory, since PHITS uses memory approximately 20 Byte / voxel
Change “param.inc” included in “src” folder
How to deal with the situation?
increase mdas: Maximum memory allowed to be used by PHITS (Byte) / 8
increase latmax: Maximum number of lattice in a cell
declare integer*8 for several parameters (see next page in detail)
Divide voxel phantom into several regions to reduce the area to be voxelized
Memory is insufficient?
Combine several CT pixels into one voxel to decrease the resolution of phantom
Delete all object files (*.o) and re-compile PHITS*
*For Windows PC, gfortran is recommended to be used for this purpose, because PHITS executable file compiled by Intel Fortran may cause “stack overflow” for large voxel phantom

## Slide 21: Notice for many materials with EGS
21
Preparation of cross-section data for EGS takes very long time if simulation geometry contains many materials (the data for all the materials will be prepared at the beginning of PHITS execution).
For repeated PHITS simulation, it is useful to keep the created cross-section data for EGS not to reconstruct the data at each time
1. Set ipegs=-1at the parameter section and execute PHITS
=> The cross-section data for EGS will be created without transport calculation
2. Set ipegs=2 at the parameter section and execute PHITS
=> Transport calculation will be conducted using the created data
For details, please refer to the parameter section for EGS in PHITS manual
How to
Many materials with EGS

## Slide 22
Table of Contents
22
Contents
How to use DICOM2PHITS
Application using DICOM2PHITS
How to use PHITS2DICOM
Notes: PHITS講習会 入門実習

## Slide 23: PHITS2DICOM
PHITS2DICOM input Signature of input file for PHITS2DICOM
data/sample.dcm Name of RTdose sample file with PATH
work/DICOM/sample010.dcm Name of Rtimage file with PATH used in DICOM2PHITS
work/PHITSinput/deposit-3D.out Name of PHITS 3D dose file with PATH
work/PHITSinput/phits.out Name of phits.out file with PATH
work/PHITSinput/RTD.deposit-3D.dcm Name of output file with PATH
0 Dose normalization 0:One for max 1:Given below
23
Convert PHITS output (3D dose distribution) into DICOM RT-dose format
2.. Create input file of PHITS2DICOM (phits2dicom.inp)
PHITS2DICOM HowTo
1. Compute 3D dose distribution by PHTIS
=> Run PHITS with phits.inp in work/PHITSinput by eliminating “OFF” at the last t-deposit
=> 3D dose distribution deposit-3D.out will be created
=> RT-dose format file will be created (work/PHITSinput/RTD.deposit-3D.dcm)
3. Execute PHITS2DICOM
Windows: Drag phits2dicom.inp and drop into dicom2phits.bat
Mac: Double click dicom2phits.command and type phits2dicom.inp + enter

## Slide 24: Check with DICOM viewer (dicompyler)
24
dicompyler: http://www.dicompyler.com/ (Free software)
Able to show RT-dose together with RT-image
Click
1. Click
2. Select “work” folder
3. Set about 30cGy
4. Click
dicompyler

## Slide 25
25
Color map appears by clicking in the squares
dicompyler
Check with DICOM viewer (dicompyler)
dicompyler: http://www.dicompyler.com/ (Free software)
Able to show RT-dose together with RT-image

## Slide 26: Application: Normalization of dose
26
1. Run PHITS2DICOM by modifying phits2dicom.inp as below
PHITS2DICOM HowTo
2. Check with DICOM viewer (dicompyler) with Rx dose = 200cGy
2 Gy at the position
(-0.23, -0.23, -1128.0)
can be confirmed !
PHITS2DICOM input Signature of input file for PHITS2DICOM
data/sample.dcm Name of RTdose sample file with PATH
work/DICOM/sample010.dcm Name of Rtimage file with PATH used in DICOM2PHITS
work/PHITSinput/deposit-3D.out Name of PHITS 3D dose file with PATH
work/PHITSinput/phits.out Name of phits.out file with PATH
work/PHITSinput/RTD.deposit-3D.dcm Name of output file with PATH
1 Dose normalization 0:One for max 1:Given below
-0.23 -0.23 -1128.0 Normalization point (x,y,z) [mm]
2.0 Normalized value

## Slide 27: Summary
27
Summary
  DICOM image data can be converted into PHITS format by using DICOM2PHITS
  Adjustment of source profile is required to fit the situation
  PHITS 3D dose distribution output can be converted to RT-dose format by using PHITS2DICOM
  Dose analysis of RT-dose by simultaneous display with RT-image using DICOM viewer (f.g. dicompyler) is feasible