## Slide 1: PHITS
Useful Functions
Multi-Purpose Particle and Heavy Ion Transport code System
Title
1
Feb. 2019 revised
Notes: PHITS講習会 入門実習

## Slide 2
Table of Contents
2
Table of Contents
[transform]
[magnetic field]
[multiplier]
[counter]
Notes: PHITS講習会 入門実習

## Slide 3
[transform]
3
X
Y
Z
Translation
Rotation
XYZ coordinate system
[transform] section
You can translate and/or rotate the spatial coordinates of [source], [surface], [cell], [magnetic field] as well as r-z and xyz meshes defined in any tallies.

## Slide 4: How to use
[transform]
4
[ Transform ]
*Trn 0 0 0 0 0 0 M
Parameter of transformation equation
M=2：translation after rotation
M=-2：rotation after translation
X-, Y-, and Z-components for translation
Rotation angles around Z-,Y-,X-axes
Transformation ID
Example 1: *tr1 0 0 10 0 45 0 0 0 0 0 0 0 2
Rotating around Y-axis by 30 degrees, and then translating along +Z-axis by 10cm.
Example 2： tr1 0 0 -10 0 pi/4 0 0 0 0 0 0 0 -2
Translating along +Z-axis by 10cm, and then rotating around Y-axis by 45 degrees.
(Note that when M=-2, direction of translation is opposite to that in M=2.)
Angle unit option
*: degree
non: radian
To define a transformation, ID and 13 parameters should be specified.
1, Define [transform] section
2, Use this [transform] by setting trcl=n in [cell], [source], etc.
six numbers should be set

## Slide 5: (Supplement) General description
[transform]
5
n: ID of transformation
O1,O2,O3: Displacement vector
B1～B9: Elements of rotation matrix
M: Parameter to change the equation of the transformation（For the case of M=-1, see manual.)
[ Transform ]
Trn O1 O2 O3 B1 B2 B3 B4 B5 B6 B7 B8 B9 M
In the case of M=1,
+
Definition with M=1,-1 can specify any rotation.

## Slide 6
track_xy.eps
[transform]
6
transform.inp
[ M a t e r i a l ]
mat[1] H 2 O 1
[ S u r f a c e ]
10 so 500.
11 cz 5.
12 pz 0.
13 pz 10.
[ C e l l ]
100 -1 10
101 1 -1. -11 12 -13
110 0 -10 #101
Execute PHITS by setting icntl=8.
track_xz.eps
Confirmation of initial setting
Cylinder with radius of 5cm and height of 10cm

## Slide 7
[transform]
7
transform.inp
[ C e l l ]
100 -1 10
101 1 -1. -11 12 -13 trcl=
110 0 -10 #101
[ Transform ]
*tr1 0 0 0 0 0 0 0 0 0 0 0 0 2
Exercise 1
Let’s rotate the cylinder around Y-axis by 30 degrees.
track_xz.eps
around Y-axis by 30 degrees
Define a transformation in [transform].
Use the defined transformation in [cell].
Rotation angles around Z-,Y-,X-axes
X-, Y-, and Z-components for translation

## Slide 8
track_xz.eps
[transform]
8
transform.inp
[ C e l l ]
100 -1 10
101 1 -1. -11 12 -13 trcl=1
110 0 -10 #101
[ Transform ]
*tr1 0 0 0 0 30 0 0 0 0 0 0 0 2
Answer 1
Rotation angle around Y-axis
Let’s rotate the cylinder around Y-axis by 30 degrees.
around Y-axis by 30 degrees

## Slide 9
[transform]
9
Move this cylinder along the positive direction of the Z-axis by 50 cm!
track_xz.eps
along the positive direction of the Z-axis by 50 cm!
transform.inp
[ C e l l ]
100 -1 10
101 1 -1. -11 12 -13 trcl=1
110 0 -10 #101
[ Transform ]
*tr1 0 0 0 0 30 0 0 0 0 0 0 0 2
Specify the Z-component for translation.
Exercise 2

## Slide 10
track_xz.eps
[transform]
10
transform.inp
[ C e l l ]
100 -1 10
101 1 -1. -11 12 -13 trcl=1
110 0 -10 #101
[ Transform ]
*tr1 0 0 50 0 30 0 0 0 0 0 0 0 2
In the cases of M=1,2, the translation is performed after the rotation.
Move this cylinder along the positive direction of the Z-axis by 50 cm!
Answer 2
along the positive direction of the Z-axis by 50 cm!

## Slide 11
[transform]
11
Let’s rotate the cylinder around Y-axis by 45 degrees, then transform it along with X-axis by 10 cm and Z-axis by 45 cm!
track_xz.eps
Reproduce this geometry
transform.inp
Change parameters of tr1.
[ C e l l ]
100 -1 10
101 1 -1. -11 12 -13 trcl=1
110 0 -10 #101
[ Transform ]
*tr1 0 0 50 0 30 0 0 0 0 0 0 0 2
step 1
step 2
step 3
Exercise 3

## Slide 12
[transform]
12
track_xz.eps
transform.inp
[ C e l l ]
100 -1 10
101 1 -1. -11 12 -13 trcl=1
110 0 -10 #101
[ Transform ]
*tr1 10 0 45 0 45 0 0 0 0 0 0 0 2
step 1
step 2
step 3
Let’s rotate the cylinder around Y-axis by 45 degrees, then transform it along with X-axis by 10 cm and Z-axis by 45 cm!
Answer 3
Reproduce this geometry

## Slide 13
[transform]
13
Construct the geometry shown below by adding a cell.
track_xz.eps
transform.inp
Do not change [surface] section.
Change [cell] & [transform] section.
(Define the transform tr2 in [transform], and then apply it to a cell 102 in [cell].)
[ C e l l ]
100 -1 10
101 1 -1. -11 12 -13 trcl=1
102 1 -1. -11 12 -13 trcl=
110 0 -10 #101 #102
[ Transform ]
*tr1 0 0 50 0 30 0 0 0 0 0 0 0 2
*tr2 0 0 0 0 0 0 0 0 0 0 0 2
Exercise 4
Reproduce this geometry

## Slide 14
[transform]
14
track_xz.eps
transform.inp
[ C e l l ]
100 -1 10
101 1 -1. -11 12 -13 trcl=1
102 1 -1. -11 12 -13 trcl=2
110 0 -10 #101 #102
[ Transform ]
*tr1 0 0 50 0 30 0 0 0 0 0 0 0 2
*tr2 0 0 30 0 0 0 0 0 0 0 0 0 2
Translation along the positive direction of the Z-axis by 30 cm!
Construct the geometry shown below by adding a cell.
Answer 4
Reproduce this geometry

## Slide 15
Table of Contents
15
Table of Contents
[transform]
[magnetic field]
[multiplier]
[counter]
Notes: PHITS講習会 入門実習

## Slide 16: [magnetic field] section
[magnetic field]
16
You can set magnetic fields (dipole and quadrupole) in certain regions in PHITS geometry to change the charged particle trajectories.
F=ev×B
Example of dipole magnet：
Homogeneous magnetic field

## Slide 17: [magnetic field] section
[magnetic field]
17
Example of quadrupole magnet：
Converge charged particle trajectory
Schematic image of quadrupole magnet
N
N
S
S
X-axis
Y-axis
You can set magnetic fields (dipole and quadrupole) in certain regions in PHITS geometry to change the charged particle trajectories.

## Slide 18: How to use
[magnetic field]
18
reg: cell ID to set the magnetic field
typ: dipole (=2) or quadrupole (=4)
gap: half distance between magnet in cm
(not used for dipole but dummy input needed)
mgf: strength of magnetic field in kG
trcl: transform ID
After defining [magnetic field] section, you can activate this function by setting imagnf=1 in [parameters].
Direction of Magnetic Field
Y-axis (positive direction) for dipole
→positive charged particles go to the negative direction of X-axis when they go to the positive direction of Z-axis
For quadrupole
→positive charged particles converge in X-axis and diverge in Y-axis when it goes to the positive direction of Z-axis
*For electrons and positrons, this function is available only when you use EGS5 (after PHITS version 2.90).
[ Magnetic Field ]
reg typ gap mgf trcl
1 4 10.0 -5.0 3
2 4 10.0 5.0 1
3 2 10.0 -10.0 0

## Slide 19
track_xz.eps
19
magfield.inp
[ S o u r c e ]
s-type = 1
proj = proton
dir = 1
r0 = 2.5
z0 = -10.
z1 = -10.
e0 = 200
[ S u r f a c e ]
10 so 500.
11 cz 5.
12 pz 0.
13 pz 10.
[ C e l l ]
100 -1 10
101 0 -11 12 -13 trcl=1
102 0 -11 12 -13 trcl=2
103 0 -11 12 -13 trcl=3
110 0 -10 #101 #102 #103
icntl=8
icntl=0
Execute PHITS by setting icntl=8 and 0.
Confirmation of initial setting
[magnetic field]

## Slide 20
20
Set dipole magnet in cell 103.
track_xz.eps
Remove a comment mark $, to set imagnf=1 in [parameters].
Confirm the setting of [Magnetic Field].
magfield.inp
[ P a r a m e t e r s ]
icntl = 0
maxcas = 1000
maxbch = 1
$ imagnf = 1
file(6) = phits.out
・ ・ ・ ・ ・ ・
[Magnetic Field]
reg typ gap mgf
103 2 10 100
Set dipole magnet
Exercise 1
[magnetic field]

## Slide 21
21
track_xz.eps
magfield.inp
[ P a r a m e t e r s ]
icntl = 0
maxcas = 1000
maxbch = 1
imagnf = 1
file(6) = phits.out
・ ・ ・ ・ ・ ・
[Magnetic Field]
reg typ gap mgf
103 2 10 100
The beam goes to the negative direction of X-axis.
Set dipole magnet in cell 103.
Answer 1
[magnetic field]

## Slide 22
22
track_xz.eps
Set typ to 4 in [Magnetic Field].
magfield.inp
[ P a r a m e t e r s ]
icntl = 0
maxcas = 1000
maxbch = 1
imagnf = 1
file(6) = phits.out
・ ・ ・ ・ ・ ・
[Magnetic Field]
reg typ gap mgf
103 2 10 100
Set quadrupole magnet
Exercise 2
Set quadrupole magnet in cell 103.
[magnetic field]

## Slide 23
23
track_xz.eps
magfield.inp
[ P a r a m e t e r s ]
icntl = 0
maxcas = 1000
maxbch = 1
imagnf = 1
file(6) = phits.out
・ ・ ・ ・ ・ ・
[Magnetic Field]
reg typ gap mgf
103 4 10 100
The beam converges in X-axis.
Set quadrupole magnet in cell 103.
Answer 2
[magnetic field]

## Slide 24
24
Check divergence of particle trajectories along to the Y-axis!
track_xz.eps
Change z-type in the [T-Track] section with axis=xy.
Set nz=3 and set z coordinates to confirm the xy-plane at z=35,45,55cm.
magfield.inp
[ T - T R A C K ]
mesh = xyz
x-type = 2
nx = 100
xmin = -25.
xmax = 25.
y-type = 2
ny = 100
ymin = -25.
ymax = 25.
z-type = 1
nz = 3
-5.0 5.0
part = proton
・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・
file = track_xy.out
Z=35, 45, 55cm
Exercise 3
[magnetic field]

## Slide 25
25
magfield.inp
[ T - T R A C K ]
mesh = xyz
x-type = 2
nx = 100
xmin = -25.
xmax = 25.
y-type = 2
ny = 100
ymin = -25.
ymax = 25.
z-type = 1
nz = 3
30.0 40.0 50.0 60.0
part = proton
・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・ ・
file = track_xy.out
track_xy.eps
Check divergence of particle trajectories along to the Y-axis!
Answer 3
[magnetic field]

## Slide 26
[ P a r a m e t e r s ]
icntl = 0
maxcas = 1000
maxbch = 1
imagnf = 1
file(6) = phits.out
・ ・ ・ ・ ・ ・
[Magnetic Field]
reg typ gap mgf
102 10
103 10
26
Bend and converge the beam to hit the cell 101 like the picture below.
(No need to consider the divergence of beam along to Y-axis).
track_xz.eps
Set two different magnetic fields.
Control the beam by changing the direction and strength of the magnetic fields.
magfield.inp
Exercise 4
[magnetic field]

## Slide 27
[ P a r a m e t e r s ]
icntl = 0
maxcas = 1000
maxbch = 1
imagnf = 1
file(6) = phits.out
・ ・ ・ ・ ・ ・
[Magnetic Field]
reg typ gap mgf
102 4 10 50
103 2 10 -150
27
track_xz.eps
magfield.inp
Bend and converge the beam to hit the cell 101 like the picture below.
(No need to consider the divergence of beam along to Y-axis).
Answer 4
[magnetic field]

## Slide 28
Table of Contents
28
Table of Contents
[transform]
[magnetic field]
[multiplier]
[counter]
Notes: PHITS講習会 入門実習

## Slide 29
[multiplier]
29
You can obtain tally results multiplied by coefficients depending on energies for [t-track], [t-cross], and [t-point].
[multiplier] section
To estimate effective dose at specified regions
→ by multiplying particle fluences by conversion coefficients of effective dose
Energy distribution of neutron fluences
Conversion coefficients based on ICRP103 (AP irradiation)

## Slide 30
[ t-track ]
・ ・ ・ ・ ・ ・
multiplier = all
mat mset1 mset2 mset3 mset4
all ( 1.0 -200 ) ( 1.0 -201 ) ( 1.0 -204 ) ( 1.0 -202 )
[multiplier]
30
ID number.
Implemented data sets and user-defined sets can be used.
Add a multiplier subsection to the tally section.
mseti: multiplier set
(maximum of six sets can be defined)
Normalization factor
multiplier subsection
Usually, “all” should be set.
How to use

## Slide 31: Implemented data sets
[multiplier]
31
Kind of data set | ID number
H*(10) | -200
Effective dose based on ICRP60 (AP irradiation) | -201
Effective dose based on ICRP103 (AP irradiation) | -202
Effective dose based on ICRP103 (ISO irradiation) | -203
New operational quantity H* | -204
Sex-averaged effective dose equivalent (ISO irradiation) | -210
Effective dose equivalent for male ・ female (ISO irradiation) | -211・-212
Dose equivalent for male ・ female red-bone marrow (ISO irradiation) | -213・-214
Dose equivalent for male ・ female skin (ISO irradiation) | -215・-216
Soft error rate on semiconductor device (ISO irradiation) | -299
Besides, values of 1/weight (ID=-1), 1/velocity (ID=-2), and material density (ID=-120) are set as the multiplication factors.

## Slide 32: Definition of multiplication factors
[multiplier]
32
You can define original coefficients to multiply tally results in [multiplier] section.
[ multiplier ]
number = -202
interpolation = log
part = neutron
ne = 68
1.0000E-09 3.0900E+00
1.0000E-08 3.5500E+00
2.5000E-08 4.0000E+00
1.0000E-07 5.2000E+00
・ ・ ・ ・ ・ ・
ID number: negative integers between -200 and -299 are available.
(The same number as that of the implemented data set can be specified.)
Interpolation method: log (logarithmic) or lin (linear)
Particle type
Number of data
Numerical data:
ne sets of energies [MeV] and strengths are given.

## Slide 33
33
track_xz.eps(1st page)
[ S o u r c e ]
s-type = 1
proj = neutron
e0 = 20
・ ・ ・ ・ ・ ・
[ M a t e r i a l ]
MAT[ 1 ]
Fe 1.0
MAT[ 2 ]
H -0.023
C -0.0023
O -1.22
・ ・ ・ ・ ・ ・
[ C e l l ]
100 -1 10
102 1 -7.86 -11 12 -13 trcl=2
103 2 -2.302 -11 12 -13 trcl=3
110 0 -10 #102 #103
icntl=8
icntl=0, neutron
multiplier.inp
[multiplier]
Execute PHITS by setting icntl=8 and 0.
Confirmation of initial setting

## Slide 34
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
z-type = 2
zmin = 30.0
zmax = 40.0
nz = 50
・ ・ ・ ・ ・ ・
axis = z
file = track_z.out
part = all
gshow = 3
epsout = 2
y-txt = Effective dose [pSv/source]
multiplier = all
mat mset1
all ( 1.0 -202 )
34
Convert the depth distribution of the particle fluence to that of the effective dose in the concrete.
Add a multiplier subsection to the [t-track] section with axis=z.
Set ID number -202 to obtain the effective dose based on ICRP103 (AP irradiation).
multiplier.inp
multiplier
subsection
Tally in the concrete region (30cm<z<40cm)
[multiplier]
Rewrite the text of the y-axis
Exercise 1

## Slide 35
35
[multiplier]
track_z.eps
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
z-type = 2
zmin = 30.0
zmax = 40.0
nz = 50
・ ・ ・ ・ ・ ・
axis = z
file = track_z.out
part = all
gshow = 3
epsout = 2
y-txt = Effective dose [pSv/source]
multiplier = all
mat mset1
all ( 1.0 -202 )
multiplier.inp
Convert the depth distribution of the particle fluence to that of the effective dose in the concrete.
Answer 1
The depth distribution of the effective dose was obtained.

## Slide 36
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
z-type = 2
zmin = 30.0
zmax = 40.0
nz = 50
・ ・ ・ ・ ・ ・
axis = z
file = track_z.out
part = all
gshow = 3
epsout = 2
y-txt = Effective dose [pSv/source]
multiplier = all
mat mset1
all ( 1.0 -202 )
multiplier.inp
36
Convert the unit of dose from pSv to mSv.
Change the normalization factor in the multiplier subsection.
Rewrite y-txt. pSv→$\mu$Sv (surround by $$ marks to use Greek alphabet)
From p(pico:10-12) to m(micro:10-6)
[multiplier]
track_z.eps
Exercise 2

## Slide 37
37
[multiplier]
track_z.eps
Values on the y-axis became small.
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
z-type = 2
zmin = 30.0
zmax = 40.0
nz = 50
・ ・ ・ ・ ・ ・
axis = z
file = track_z.out
part = all
gshow = 3
epsout = 2
y-txt = Effective dose [$\mu$Sv/source]
multiplier = all
mat mset1
all ( 1e-6 -202 )
multiplier.inp
Convert the unit of dose from pSv to mSv.
Answer 2

## Slide 38
Table of Contents
38
Table of Contents
[transform]
[magnetic field]
[multiplier]
[counter]
Notes: PHITS講習会 入門実習

## Slide 39: What is “Counter” in PHITS?
[counter]
39
Each particle has its own “Counter” number to identify what it has been experienced, such as entering, exiting from, reacting in, and reflected by a certain region.
To investigate the origin of the tallied particles
→ What is the difference between particles
produced in different regions?
Tally
When a particle reacts in a region, count = counter +1.

## Slide 40: How to use
[ Counter ]
counter = 1
part = neutron proton
reg in out coll ref
1 1 10000 0 0
2 1 10000 0 0
[counter]
40
Action
0: Nothing happens
10000: Set counter = 0 (Reset)
Other: Counter = Counter + specified Number
*You can distinguish further detailed channels for coll. (See the next slide.)
1, Define [counter] section
2, Use this function by setting ctmin(i), ctmax(i) in each tally section (i is counter ID).
Cells to activate this counter
Event Types
in: Enter the cell
out: Exit from the cell
coll: React in the cell*
ref: Reflected by the cell
Counter: counter ID (up to 3)
part: Particle species to which this counter is applied.

## Slide 41: Detailed classification of coll
[counter]
41
atom: atomic interactions
delt: delta-ray production
knoe: knock-on electrons production by electrons and positrons
fluo: fluorescence x-ray production
auge: Auger electron production
brem: Bremsstrahlung
phel: photoelectric effect
cmpt: Compton scatterings
pprd: electron-positron pair production
anih: electron-positron pairs annihilation
coll is classified as nucl, atom, and dcay. Furthermore, nucl and atom have 3 and 8 channels, respectively.
dcay: particle decays
nucl: nuclear interactions
elst: elastic scatterings
iels: inelastic scatterings
fiss: fissions
coll: reactions

## Slide 42
[counter]
42
counter.inp
Execute PHITS by setting icntl=8 and 0.
Confirmation of initial setting
track_xz.eps(1st page)
[ S o u r c e ]
s-type = 1
proj = neutron
e0 = 150
・ ・ ・ ・ ・ ・
[ M a t e r i a l ]
MAT[ 1 ]
Fe 1.0
MAT[ 2 ]
H -0.023
C -0.0023
O -1.22
・ ・ ・ ・ ・ ・
[ C e l l ]
100 -1 10
102 1 -7.86 -11 12 -13 trcl=2
103 2 -2.302 -11 12 -13 trcl=3
110 0 -10 #102 #103
icntl=8
icntl=0, neutron

## Slide 43: Confirmation of [t-track]
[counter]
43
track_z.eps
Depth distribution of effective dose based on ICRP103(AP irradiation) in the concrete.
counter.inp
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
z-type = 2
zmin = 30.0
zmax = 40.0
nz = 50
e-type = 1
ne = 1
0.0 5000.0
unit = 1
axis = z
file = track_z.out
part = all
gshow = 3
epsout = 2
angel = ymin(1.E-6) ymax(6.E-6)
y-txt = Effective dose [$\mu$Sv/source]
multiplier = all
mat mset1
all ( 1e-6 -202 )

## Slide 44
44
counter.inp
[ C o u n t e r ]
counter = 1
part = neutron
reg coll
102 1
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
file = track_z-c0.out
・ ・ ・ ・ ・ ・
multiplier = all
mat mset1
all ( 1e-6 -202 )
ctmin(1) = 0
ctmax(1) = 0
When a neutron occurs a collision in cell 102, its counter increases by 1.
[counter]
Estimate contribution of neutrons do NOT scatters in the iron material to the dose.
How much is the contribution of high-energy neutrons passing through the iron?
Exercise 1
Copy & paste the [t-track] section with axis=z.
In one of the sections, add ctmin(1)=0 and ctmax(1)=0, and change the output file name.
Min & Max values of the counter ID1 for tallied particle

## Slide 45
45
counter.inp
[counter]
track_z.eps
track_z-c0.eps
High-energy neutrons which don’t scatter in the iron have dominant contribution to the dose in the deep region of the concrete.
Unscattered particles in iron
Total
[ C o u n t e r ]
counter = 1
part = neutron
reg coll
102 1
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
file = track_z-c0.out
・ ・ ・ ・ ・ ・
multiplier = all
mat mset1
all ( 1e-6 -202 )
ctmin(1) = 0
ctmax(1) = 0
Answer 1
Estimate contribution of neutrons which do NOT scatter in the iron material to the dose.

## Slide 46
46
Copy & paste the [t-track] section with axis=z again.
In the third [t-track] section, set only ctmin(1)=1.
Change the output file name.
counter.inp
[counter]
[ C o u n t e r ]
counter = 1
part = neutron
reg coll
102 1
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
file = track_z-c1.out
・ ・ ・ ・ ・ ・
multiplier = all
mat mset1
all ( 1e-6 -202 )
ctmin(1) = 1
Exercise 2
Estimate contribution of neutrons scatter in the iron material to the dose.
Minimum value of the counter ID1 for tallied particle

## Slide 47
track_z-c1.eps
track_z-c0.eps
47
counter.inp
[counter]
[ C o u n t e r ]
counter = 1
part = neutron
reg coll
102 1
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
file = track_z-c1.out
・ ・ ・ ・ ・ ・
multiplier = all
mat mset1
all ( 1e-6 -202 )
ctmin(1) = 1
Total
Scattered particles have main contribution in the surface region of the concrete.
Answer 2
Estimate contribution of neutrons scatter in the iron material to the dose.
track_z.eps
Unscattered particles in iron
Scattered particles in iron

## Slide 48: Summary
Summary
48
Use [transform] section to translated/rotated geometrical components, source and tallies.
Use [magnetic field] section to apply magnetic field to charged particles.
Use multiplier subsection and [multiplier] section to estimate effective dose or operational quantity easily.
Use [counter] section to filter particles scored by tallies based on their detailed origin.
Notes: 《休憩はさむ》
まとめ