## Slide 1
Basic Lecture II:
Definition of Tally
Title
May 2021 revised
Notes: PHITS講習会 基礎実習

## Slide 2
Purpose
Learn how to deduce various physics quantities from PHITS simulations
Purpose of This Lecture
You can obtain this kind of results at the end of this lecture.
Particle fluence (left) and depth-dose distribution (right) for the simulation condition for homework.

## Slide 3: Contents of Lecture II
Contents
  What is Tally?
Introduction and usage of “Tally”
  How to use Tally for checking geometry
  How to use Tally for calculating physical quantities
Kinds of Tally
Summary

## Slide 4: What is Tally?
In PHITS, the word of “Tally” used for functions to
Deduce physical quantities such as flux and deposition energy,
or
Depict the 2D or 3D geometry in certain area.
What is tally?
Tally: a record of the number or amount of something, especially one that you can keep adding to;
[Oxford Advanced Learner’s Dictionary (7th edition), OXFORD.]

## Slide 5: Concept of Tally
PHITS simulates the motion of each particle using the Monte Carlo method. You can estimate their average behavior by calculating various physical quantities, such as flux and deposition energy in a certain region, by using “Tally”.
What is tally?
Result of [T-Track] (Track-length tally)
How many particles were passed through this region?
→ Use “track-length” tally.

## Slide 6
Kinds of Tally in PHITS
For example…
Calculating physical quantity
  Particle fluence → [T-Track], [T-Cross]
  Deposition energy (heat) → [T-Deposit], [T-Deposit2]
  Secondary particles → [T-Yield], [T-Product]
  LET or microdosimetric distribution → [T-LET], [T-SED]
Checking geometry
  2-dimensional visualization → gshow option, [T-Gshow], [T-Rshow]
  3-dimensional visualization → [T-3Dshow]
Tally Types
Various tally functions are implemented in PHITS.
Many physical quantities can be deduced from the PHITS simulation by selecting an appropriate tally.

## Slide 7: Contents of Lecture II
Contents
  What is Tally?
Introduction and usage of “Tally”
  How to use Tally for checking geometry
  How to use Tally for calculating physical quantities
Kinds of Tally
Summary

## Slide 8: Geometry Check
Every time you construct a new geometry, it is better to check the geometry using [T-Track] with the gshow option (2D), [T-3Dshow] (3D) or PHIG-3D (3D).
Tally for checking geometry
Otherwise you would obtain wrong results without noticing miss-definition of the geometry, especially when you make an overlapped region!

## Slide 9: Exercise 1
Tally for checking geometry
[ M a t e r i a l ]
mat[1] H 2 O 1
・ ・ ・ ・ ・ ・
[ S u r f a c e ]
10 so 500.
11 cz 10.
12 pz 0.
13 pz 50.
[ C e l l ]
100 -1 10
101 1 -1. -11 12 -13
110 0 -10 #101
A water cylinder with a radius of 10 cm and a height of 50 cm.
lec02.inp
50 cm
10 cm
Set icntl = 8 in [Parameters] section and execute PHITS.
(You have to set icntl = 8, when you use gshow option in tallies.)
Confirm the geometry of lec02.inp in a 2-dimensional view using gshow option in [T-Track] tally.

## Slide 10: Answer 1
Tally for checking geometry
track_xz.eps
track_xy.eps
xy-plane
xz-plane
The height is 50 cm.
The radius is 10 cm.
[ P a r a m e t e r s ]
icntl = 8
・ ・ ・ ・ ・ ・
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
axis = xy
file = track_xy.out
part = all
gshow = 3
epsout = 1
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
axis = xz
file = track_xz.out
part = all
gshow = 3
epsout = 1
Gshow option
lec02.inp
Confirm the geometry of lec02.inp in a 2-dimensional view using gshow option in [T-Track] tally.

## Slide 11: Exercise 2
How is this geometry shown in 3 dimensions?
Tally for checking geometry
track_xy.eps
track_xz.eps
Windows: Right-click “lec02.inp”, and select “Send to” -> “PHIG-3D”.
macOS: Drag and drop “lec02.inp” to the PHIG-3D icon in the Dock.
Linux: move to the “lec02” folder, and type “phits3d.sh lec02.inp”.
Confirm the geometry of lec02.inp in a 3-dimensional view using PHIG-3D.

## Slide 12
Tally for checking geometry
Answer 2
Geometry can be rotated by mouse.
Confirm the geometry of lec02.inp in a 3-dimensional view using PHIG-3D.

## Slide 13: Contents of Lecture II
Contents
  What is Tally?
Introduction and usage of “Tally”
  How to use Tally for checking geometry
  How to use Tally for calculating physical quantities
Kinds of Tally
Summary

## Slide 14: How to define Tally
Tally for calculating physical quantities
what physical quantities
Select types of tally: [T-Track], [T-Deposit] etc.
in where
Select geometrical mesh: mesh = reg, xyz, r-z
of what particle
Select particle type: part = neutron, proton etc.
in which unit e.g. (cm/source), (1/cm2/source) etc.
Select unit: unit = 1, 2, 3 …
in what output form
Select output axis: axis = eng, reg, xy, etc.
You have to determine …

## Slide 15
Tally for calculating physical quantities
Example of [T-Track] tally in lec02.inp
[ T - T r a c k ]
title = Track Detection in xyz mesh
mesh = xyz
x-type = 2
nx = 25
xmin = -25.
xmax = 25.
y-type = 2
ny = 25
ymin = -25.
ymax = 25.
z-type = 1
nz = 1
-5.0 5.0
e-type = 1
ne = 1
0.0 5000.0
unit = 1
axis = xy
file = track_xy.out
part = all
gshow = 3
epsout = 1
Geometrical mesh
Particle type
Unit of output
Output form
[T-Track] can be useful for visualizing particle trajectories by setting a fine mesh in the tally region.
[T-Track]: Tally for calculating track-lengths or fluences of particles in certain regions.

## Slide 16: Visualize Particle Trajectory
x-axis
z-axis
Tally for calculating physical quantities

## Slide 17
x-axis
z-axis
Visualize Particle Trajectory
Tally for calculating physical quantities

## Slide 18
x-axis
z-axis
Visualize Particle Trajectory
Tally for calculating physical quantities

## Slide 19
x-axis
z-axis
Visualize Particle Trajectory
Tally for calculating physical quantities

## Slide 20
x-axis
z-axis
Visualize Particle Trajectory
Tally for calculating physical quantities

## Slide 21: Exercise 3
Confirm particle fluence by using [T-Track].
Tally for calculating physical quantities
Set “icntl = 0” in [Parameters] section and execute PHITS.
What is the behavior of the particles?
[ P a r a m e t e r s ]
icntl = 8
・ ・ ・ ・ ・ ・
[ S o u r c e ]
s-type = 1
r0 = 2.5
z0 = -10.
z1 = -10.
dir = 1.0
e0 = 250.
proj = 12C
A carbon beam at 250 MeV/u with a radius of 2.5 cm
Open the track-xy.eps and track-xz.eps.
lec02.inp

## Slide 22
Tally for calculating physical quantities
Answer 3
Confirm particle fluence by using [T-Track].
file = :
Define output file name.
epsout = 1:
Generate eps file. The eps file name will be picked up from output file name.
（e.g. track_xz.out → track_xz.eps）
[ P a r a m e t e r s ]
icntl = 0
・ ・ ・ ・ ・ ・
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
axis = xy
file = track_xy.out
part = all
gshow = 3
epsout = 1
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
axis = xz
file = track_xz.out
part = all
gshow = 3
epsout = 1
For 2D-plots, error files (***_err.out, ***_err.eps) are automatically generated.
lec02.inp

## Slide 23
Tally for calculating physical quantities
Answer 3
Confirm particle fluence by using [T-Track].
lec02.inp
[ P a r a m e t e r s ]
icntl = 0
・ ・ ・ ・ ・ ・
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
axis = xy
file = track_xy.out
part = all
gshow = 3
epsout = 1
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
axis = xz
file = track_xz.out
part = all
gshow = 3
epsout = 1
track_xz.eps
track_xy.eps

## Slide 24: Error file (*_err.eps)
Tally for calculating physical quantities
In 2D-plots such as tallies with “axis = xy, xz”, statistical errors are output in another file named ***_err.eps.
Warmer colors indicate larger relative standard errors (closer to 1), while colder colors mean smaller errors.
track_xy_err.eps
track_xz_err.eps

## Slide 25: Red Screen
Tally for calculating physical quantities
track_xy.eps for dir = -1.0
If no particle is scored in a tally, all regions are painted in red
→ usually something is wrong with the input file!!

## Slide 26: How to define Tally
Tally for calculating physical quantities
what physical quantities
Select types of tally: [T-Track], [T-Deposit] etc.
in where
Select geometrical mesh: mesh = reg, xyz, r-z
of what particle
Select particle type: part = neutron, proton etc.
in which unit e.g. (cm/source), (1/cm2/source) etc.
Select unit: unit = 1, 2, 3 …
in what output form
Select output axis: axis = eng, reg, xy, etc.
You have to determine …

## Slide 27
xyz mesh:
Divide the regions in the XYZ coordinates.
X
Y
Z
Geometrical Mesh Types
There are 3 types of geometrical mesh in PHITS.
Z
R
r-z mesh:
Divide the regions in
the Cylindrical coordinates.
reg mesh:
Divide the regions in
cells defined in the
PHITS virtual space.
Tally for calculating physical quantities

## Slide 28
Tally for calculating physical quantities
Geometrical Mesh
mesh = xyz :
Define tally region according to the xyz coordinate system.
⇒ x-type, y-type, z-type subsections
are required to define each mesh.
X-axis (x-type = 2)
xmin : minimum value
xmax : maximum value
nx : number of bins
Z-axis (z-type = 1)
nz : (number of bins)
-5.0 5.0 : (Boundaries of bins）
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
mesh = xyz
x-type = 2
nx = 25
xmin = -25.
xmax = 25.
y-type = 2
ny = 25
ymin = -25.
ymax = 25.
z-type = 1
nz = 1
-5.0 5.0
e-type = 1
ne = 1
0.0 5000.0
t-type = 1
nt = 1
0.0 1.0e+6
・ ・ ・ ・ ・ ・
lec02.inp

## Slide 29
1: Define # of bins
and their boundaries.
2,3: Define # of bins, and the range (min & max values).
Mesh is divided equally by linear scale (= 2) or log scale (= 3).
How to Define a Mesh
Mesh is a common concept used in many tallies.
x-type, y-type, z-type, r-type, e-type, t-type, a-type etc.
x-axis y-axis z-axis radius energy time angle
There are 5 types to define a mesh as follows. (types 4 & 5 are rarely used)
4,5: Define the range of the mesh (min & max values) and xdel for the mesh width.
(= 5: xdel is given by log value of mesh interval)
Tally for calculating physical quantities
x-type = 1
nx = 10
0 1 2 3 5 10
15 20 30 50 100
x-type = 2
nx = 100
xmin = 0
xmax = 1000
x-type = 3
nx = 100
xmin = 0.1
xmax = 5000
Replace “x” to “y”, “z”, “r”, “e” , “t” , or “a” if you want to define other meshes.
(e.g. y-type, ny, ymin)

## Slide 30: Exercise 4
To see a finer structure in a 2D plot, increase # of bins in the [T-Track].
Multiply nx and ny in the [T-Track] section with “axis = xy” by 4.
Multiply nx and nz in the [T-Track] section with “axis = xz” by 4.
Tally for calculating physical quantities
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
mesh = xyz
x-type = 2
nx = 25
・ ・ ・ ・ ・ ・
y-type = 2
ny = 25
・ ・ ・ ・ ・ ・
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
mesh = xyz
x-type = 2
nx = 25
・ ・ ・ ・ ・ ・
z-type = 2
nz = 50
・ ・ ・ ・ ・ ・
lec02.inp
track_xz.eps
track_xy.eps

## Slide 31
Tally for calculating physical quantities
We can see the tracks with a better resolution by increasing nx and ny.
Answer 4
To see a finer structure in a 2D plot, increase # of bins in the [T-Track].
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
mesh = xyz
x-type = 2
nx = 100
・ ・ ・ ・ ・ ・
y-type = 2
ny = 100
・ ・ ・ ・ ・ ・
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
mesh = xyz
x-type = 2
nx = 100
・ ・ ・ ・ ・ ・
z-type = 2
nz = 200
・ ・ ・ ・ ・ ・
lec02.inp
track_xz.eps
track_xy.eps

## Slide 32: Exercise 5
To see a change of fluence with a time, subdivide the time mesh in the [T-Track].
Edit t-type sub-section in the [T-Track] section with “axis=xz”.
Set “t-type = 2” and set nt, tmin, tmax to be 5, 0.0, 5.0, respectively.
(See “How to Define a Mesh” in p. 29.)
Delete or comment out the unnecessary line.
Tally for calculating physical quantities
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
e-type = 1
ne = 1
0.0 5000.0
t-type = 1
nt = 1
0.0 1.0e+9
・ ・ ・ ・ ・ ・
lec02.inp

## Slide 33: Answer 5
To see a change of fluence with a time, subdivide the time mesh in the [T-Track].
Tally for calculating physical quantities
1st page
（t = 0 ~ 1 nsec）
2nd page
（t = 1 ~ 2 nsec）
3rd page
（t = 2 ~ 3 nsec）
track_xz.eps
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
e-type = 1
ne = 1
0.0 5000.0
t-type = 2
nt = 5
$ 0.0 1.0e+9
tmin = 0.0
tmax = 5.0
・ ・ ・ ・ ・ ・
lec02.inp
In GSview, the pages of *.eps can be switched by space and backspace keys.
The GIF animation can be made. (See phits/utility/animation)

## Slide 34: How to define Tally
Tally for calculating physical quantities
what physical quantities
Select types of tally: [T-Track], [T-Deposit] etc.
in where
Select geometrical mesh: mesh = reg, xyz, r-z
of what particle
Select particle type: part = neutron, proton etc.
in which unit e.g. (cm/source), (1/cm2/source) etc.
Select unit: unit = 1, 2, 3 …
in what output form
Select output axis: axis = eng, reg, xy, etc.
You have to determine …

## Slide 35: Exercise 6
Replace “part = all” in the [T-Track] tally with “axis = xz” by “part = 12C proton neutron”.
Restore t-type subsection to the original settings.
(i.e. “t-type = 1”)
Tally for calculating physical quantities
Show the fluences of individual particle species.
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
t-type = 2
nt = 5
$ 0.0 1.0e+9
tmin = 0.0
tmax = 5.0
・ ・ ・ ・ ・ ・
axis = xz
file = track_xz.out
part = all
・ ・ ・ ・ ・ ・
lec02.inp
track_xz.eps
What are the individual behaviors of 12C, protons, and neutrons?

## Slide 36
Tally for calculating physical quantities
Answer 6
track_xz.eps
1st page
(part = 12C)
2nd page
(part = proton)
3rd page
(part = neutron)
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
t-type = 1
nt = 1
0.0 1.0e+9
$ tmin = 0.0
$ tmax = 5.0
・ ・ ・ ・ ・ ・
axis = xz
file = track_xz.out
part = 12C proton neutron
・ ・ ・ ・ ・ ・
lec02.inp
Show the fluences of individual particle species.

## Slide 37: How to define Tally
Tally for calculating physical quantities
what physical quantities
Select types of tally: [T-Track], [T-Deposit] etc.
in where
Select geometrical mesh: mesh = reg, xyz, r-z
of what particle
Select particle type: part = neutron, proton etc.
in which unit e.g. (cm/source), (1/cm2/source) etc.
Select unit: unit = 1, 2, 3 …
in what output form
Select output axis: axis = eng, reg, xy, etc.
You have to determine …

## Slide 38: Exercise 7
Show the particle fluence with its energy distribution.
Tally for calculating physical quantities
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
x-type = 2
nx = 100
・ ・ ・ ・ ・ ・
z-type = 2
nz = 200
・ ・ ・ ・ ・ ・
e-type = 1
ne = 1
0.0 5000.0
unit = 1
axis = xz
file = track_xz.out
・ ・ ・ ・ ・ ・
lec02.inp
Replace “axis = xz” by “axis = eng”.
Set “e-type = 2” and set ne, emin, and emax to be 100, 0.0, and 5000.0, respectively.
(See “How to Define a Mesh” in p. 29.)
Set “nx = 1” and “nz = 1” to reduce the number of pages in the output.
Change the output file name to “track_eng.out”.

## Slide 39
Tally for calculating physical quantities
Answer 7
Show the particle fluence with its energy distribution.
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
x-type = 2
nx = 1
・ ・ ・ ・ ・ ・
z-type = 2
nz = 1
・ ・ ・ ・ ・ ・
e-type = 2
ne = 100
$ 0.0 5000.0
emin = 0.0
emax = 5000.0
unit = 1
axis = eng
file = track_eng.out
・ ・ ・ ・ ・ ・
lec02.inp
track_eng.eps
The beam energy is 250×12=3000MeV
In the default setting, emin and emax are defined in the unit of “MeV”. If you want to defined them in the unit of “MeV/u”, specify “iMeVperU = 1” in [Parameter] section.

## Slide 40: Exercise 8
Change the horizontal axis to a logarithmic scale.
Tally for calculating physical quantities
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
x-type = 2
nx = 1
・ ・ ・ ・ ・ ・
z-type = 2
nz = 1
・ ・ ・ ・ ・ ・
e-type = 2
ne = 100
$ 0.0 5000.0
emin = 0.0
emax = 5000.0
unit = 1
axis = eng
file = track_eng.out
・ ・ ・ ・ ・ ・
lec02.inp
track_eng.eps
This figure is shown in linear scale.
Set “e-type=3” and “emin=1.0”.

## Slide 41
Tally for calculating physical quantities
We can check the low energy region in detail.
Answer 8
Change the horizontal axis to a logarithmic scale.
[ T - T r a c k ]
・ ・ ・ ・ ・ ・
x-type = 2
nx = 1
・ ・ ・ ・ ・ ・
z-type = 2
nz = 1
・ ・ ・ ・ ・ ・
e-type = 3
ne = 100
$ 0.0 5000.0
emin = 1.0
emax = 5000.0
unit = 1
axis = eng
file = track_eng.out
・ ・ ・ ・ ・ ・
lec02.inp
track_eng.eps

## Slide 42: Exercise 9
Tally for calculating physical quantities
[ T - T r a c k ]
mesh = xyz
x-type = 2
nx = 1
xmin = -25.
xmax = 25.
y-type = 1
ny = 1
-5.0 5.0
z-type = 2
nz = 1
zmin = -20.
zmax = 80.
・ ・ ・ ・ ・ ・
lec02.inp
Delete
or
Comment out
Add “reg” parameter
Change the geometrical mesh from the xyz mesh to the reg mesh.
Add “reg” parameter and define cell numbers of inside and outside of the cylinder.
The cell numbers of inside and outside of the cylinder are 101 and 110, respectively.
Delete or comment out parameters for “mesh = xyz” sub-section.
Show the energy distributions inside and outside of the cylinder.

## Slide 43: Answer 9
Tally for calculating physical quantities
[ T - T r a c k ]
mesh = reg
reg = 101 110
$ x-type = 2
$ nx = 1
$ xmin = -25.
$ xmax = 25.
$ y-type = 1
$ ny = 1
$ -5.0 5.0
$ z-type = 2
$ nz = 1
$ zmin = -20.
$ zmax = 80.
・ ・ ・ ・ ・ ・
lec02.inp
track_eng.eps
1st page
(reg = 101: water)
2nd page
(reg = 110: void)
Show the energy distributions inside and outside of the cylinder.

## Slide 44: Exercise 10
Tally for calculating physical quantities
[ T - D e p o s i t ]
title = Energy deposition in xyz mesh
mesh = xyz
・ ・ ・ ・ ・ ・
unit = 1
material = all
output = dose
axis = xz
file = deposit.out
part = all
gshow = 1
epsout = 1
t-deposit.inp
[T-Deposit]: Tally for calculating deposited energy in materials
Copy [T-Deposit] section from t-deposit.inp and paste it in lec02.inp.
Execute PHITS with the input file of lec02.inp.
Confirm spatial distribution of deposited energies (i.e. dose) in water cylinder using [T-Deposit].

## Slide 45: Answer 10
Tally for calculating physical quantities
deposit.eps
Energy deposition by the carbon beam.
Energy deposition by the secondary particles.
Confirm spatial distribution of deposited energies (i.e. dose) in water cylinder using [T-Deposit].

## Slide 46: How to define Tally
Tally for calculating physical quantities
what physical quantities
Select types of tally: [T-Track], [T-Deposit] etc.
in where
Select geometrical mesh: mesh = reg, xyz, r-z
of what particle
Select particle type: part = neutron, proton etc.
in which unit e.g. (cm/source), (1/cm2/source) etc.
Select unit: unit = 1, 2, 3 …
in what output form
Select output axis: axis = eng, reg, xy, etc.
You have to determine …

## Slide 47: Exercise 11
Tally for calculating physical quantities
Change the unit of the output in the [t-deposit] tally from [MeV/cm3/source] to [Gy/source].
[ T - D e p o s i t ]
・ ・ ・ ・ ・ ・
unit = 1
material = all
output = dose
axis = xz
file = deposit.out
part = all
gshow = 1
epsout = 1
lec02.inp
The concept of the (/source) will be learned in the basic lecture III.
Replace “unit = 1” by “unit = 0”.
Note: When a region includes more than two materials, the calculated dose in such a region does not equal to average value of the region.
[PHITS] [average dose]
Calculating the deposit energy in units of Gy = J/kg.

## Slide 48: Answer 11
Tally for calculating physical quantities
Change the unit of the output in the [t-deposit] tally from [MeV/cm3/source] to [Gy/source].
deposit.eps
[ T - D e p o s i t ]
・ ・ ・ ・ ・ ・
unit = 0
material = all
output = dose
axis = xz
file = deposit.out
part = all
gshow = 1
epsout = 1
lec02.inp
The unit and its scale have changed.

## Slide 49: Exercise 12
Tally for calculating physical quantities
Show the energy deposition along the z-axis in the water cylinder by using an r-z mesh.
[ T - Deposit ]
・ ・ ・ ・ ・ ・
mesh = xyz
x-type = 2
nx = 100
xmin = -25.
xmax = 25.
y-type = 1
ny = 1
-5.0 5.0
z-type = 2
nz = 200
zmin = -20.
zmax = 80.
・ ・ ・ ・ ・ ・
axis = xz
file = deposit.out
・ ・ ・ ・ ・ ・
lec02.inp
Delete
or
Comment out
Change to r-type
Change the geometrical mesh from the xyz mesh to the r-z mesh.
Delete of comment out the parameters for x-type sub-section.
Change y-type sub-section to r-type sub-section and set radial range from 0 to 10 cm within 1 bin.
Replace “axis=xz” by “axis=z”.
Z
R
Plot the depth distribution of the energy deposition with an r-z mesh.

## Slide 50
Tally for calculating physical quantities
A Bragg peak of the carbon beam is shown at z=12 cm.
[ T - Deposit ]
・ ・ ・ ・ ・ ・
mesh = r-z
$ x-type = 2
$ nx = 100
$ xmin = -25.
$ xmax = 25.
r-type = 1
nr = 1
0.0 10.0
z-type = 2
nz = 200
zmin = -20.
zmax = 80.
・ ・ ・ ・ ・ ・
axis = z
file = deposit.out
・ ・ ・ ・ ・ ・
lec02.inp
deposit.eps
Show the energy deposition along the z-axis in the water cylinder by using an r-z mesh.
Answer 12

## Slide 51: Graphic utility ANGEL
Tally for calculating physical quantities
What is ANGEL?
A software to convert text data files (*.out) to image files (*.eps).
You can adjust regions of vertical axes by setting angel parameter in the tally sections. (See the ANGEL manual for details of angel parameters)
You can write angel parameters to the *.out files directly.
You can execute ANGEL only by ”right-click→send to→ANGEL” (Windows) or “drag&drop to the ANGEL ion” (Mac).
(You don’t have to execute PHITS again only to re-draw the image files.)
For example, add
p: ymin(1e-11) ymax(1e-9)
to deposit.out, and then execute ANGEL.
The range of the vertical axis changes.

## Slide 52
Purpose
A free software for 3D visualization.
Draw 3D view of tally results for mesh = xyz.
You can output tally results in ParaView format (*.vtk) by specifying “vtkout = 1” in each tally section.
ParaView + PHITS sample (lecture\advanced\ParaView)
http://www.paraview.org
3D visualization software ParaView
Notes: 「実習」 前の基本的な話から

## Slide 53: Contents of Lecture II
Contents
  What is Tally?
Introduction and usage of “Tally”
  How to use Tally for checking geometry
  How to use Tally for calculating physical quantities
Kinds of Tally
Summary

## Slide 54
List of Tallies (Visualize geometry)
[T-Gshow] | 2D geometry visualization
[T-Rshow] | 2D geometry visualization with physical quantities
[T-3Dshow] | 3D geometry visualization

## Slide 55
Kinds of tally in PHITS
[T-Gshow]
Tally for visualizing the geometry in 2 dimensions cut by certain slices.
Show region boundary, cell number, material ID etc.
Other tallies can be used for this purpose by setting icntl=8 in the [Parameters] section (see Lecture I).

## Slide 56
Kinds of tally in PHITS
[T-3Dshow]
Tally for visualizing the geometry in 3 dimensions from a viewpoint of a certain location in PHITS virtual space.
Activated only when icntl = 11 in the [Parameters] section.

## Slide 57
Origin (x0,y0,z0)
(e-the,e-phi,e-dst)
w-hgt
(w-mnh)
w-dst
w-wdt
(w-mnw)
e-dst
Picture Flame
Eye Point
Light source
(l-the,l-phi,l-dst)
w-mnw × w-mnh ＝ #Pixel
100 × 100 (default)
Spherical Coordinates
Spherical coordinates
XYZ-coordinates
Tally for checking geometry
Parameters used in [T-3Dshow]

## Slide 58
Tally for checking geometry
You can rotate [T-3Dshow] picture using Python software.
See “/phits/utility/animation/rotate3dshow” in more detail.
[T-3Dshow] (for your FUN!)

## Slide 59
Kinds of tally in PHITS
[T-Track] | Particle fluence in a certain region
[T-Cross] | Particle fluence/current across a certain surface
[T-Point] | Particle fluence at a certain point
[T-Deposit] | Deposit energy in a certain region
[T-Deposit2] | Deposit energies in two certain regions
[T-Yield] | Residual nuclei yield in a certain region
[T-Product] | Produced particle in a certain region
[T-DPA] | Displacement Per Atom (DPA) in a certain region
[T-LET] | LET distribution in a certain region
[T-SED] | Microdosimetric quantity distribution in a certain region
[T-Interact] | Number of interactions in a certain region
[T-DCHAIN] | Residual nuclide yields (in combination with DCHAIN)
[T-Time] | Time information of particle in a certain region
[T-Adjoint] | Particle fluence in a certain region with adjoint mode calculation
[T-Volume] | Volumes of a certain cell
[T-WWG] | Parameters used for the [Weight Window] section
[T-WWBG] | Parameters used for the [WW Bias] section
[T-Userdefined] | Any user-defined quantities
List of Tallies (Deduce physical quantity)
Described in the following pages.

## Slide 60
Kinds of tally in PHITS
[T-Track]
You can visualize the trajectory of particle using [T-Track] by setting small mesh for tallying regions.
Tally for calculating track-length (cm) of particles in certain regions.
Average fluence (/cm2) in the region can be also deduced from this tally, dividing the track length (cm) by the volume of the region (cm3).

## Slide 61
Kinds of tally in PHITS
direction of particle trajectory
[T-Cross]
Tally for calculating fluence or current (/cm2) of particles across certain surfaces.
Current is simply added by 1 when a particle cross the surface, while flux is added by 1/cos(θ).

## Slide 62
Kinds of tally in PHITS
[T-Point]
[T-Track]
Neutron and photon fluences calculated by [T-Point] and [T-Track] for similar conditions.
[T-Point]
Tally for calculating fluence (/cm2) of neutron and/or photon at a certain point or ring.
There are some using limitations. (See phits/utility/tpoint)

## Slide 63
Kinds of tally in PHITS
Bragg peak calculated by [T-Deposit] tally
[T-Deposit]
Tally for calculating deposition energy (MeV) in certain regions.
Ionization energy losses by charged particles are scored. → Event-by-event data can be also deduced!
Neutron and photon doses can be also calculated by the kerma approximation.

## Slide 64
Kinds of tally in PHITS
Example of [T-Deposit2] tally
[T-Deposit2]
Tally for calculating event-by-event deposition energies in two regions.
Output a 2D plot to show their correlation.
Useful for simulating experimental data obtained by using two detectors.

## Slide 65
Kinds of tally in PHITS
Example of [T-Yield]
[T-Yield], [T-Product]
Tally for calculating the number of secondary particles generated by nuclear reactions in certain regions.
Energy or time distribution of secondary particles can be obtained from [T-Product].
Yields of each nuclide can be depicted on nuclear chart with [T-Yield].

## Slide 66
Kinds of tally in PHITS
Depth-DPA distribution calculated using [T-DPA]
[T-DPA]
Tally for calculating the radiation damage index DPA in certain regions.
DPA is the average number of displaced atoms per atom of a material, and is calculated by multiplying the fluence with the damage cross section.

## Slide 67
Kinds of tally in PHITS
Example of [T-LET] tally
*SED represents
Specific Energy Distribution
[T-LET], [T-SED]
Tally for calculating the probability densities of deposition energy or fluence in terms of LET, lineal energy (y), or specific energy (z) in microscopic sites distributed in certain regions.
Useful for radiobiological calculations.

## Slide 68
Kinds of tally in PHITS
Example of [T-Interact] tally
[T-Interact]
Tally for calculating the number of interactions occurred in certain regions.
The mean number or probability density of interactions can be obtained.

## Slide 69
Please see recommendation/dchain in detail
Time-dependent radioactivities of a water phantom irradiated by 150-MeV protons for 6 min.
[T-DCHAIN]
Tally for generating input files for DCHAIN, which can calculate the time evolution of the radioactive nuclides during and after irradiation.
DCHAIN is also included in the PHITS package.

## Slide 70: Contents of Lecture II
Contents
  What is Tally?
Introduction and usage of “Tally”
  How to use Tally for checking geometry
  How to use Tally for calculating physical quantities
Kinds of Tally
Summary

## Slide 71
Summary
A variety of information can be deduced from the PHITS simulation using functions called “Tally”.
2 types of tallies are implemented in PHITS, one is for visualizing PHITS geometry, and the other is for calculating physical quantities.
For defining tally, you have to determine …
You can find examples of each tally in the “phits/sample/tally” folder.
Summary
what physical quantities
in where
of what particle
in which unit
in what output form

## Slide 72
Homework
Depict the neutron and proton fluences, respectively, in your homework.
Adjust [t-deposit] to see the Bragg peak of proton.
Investigate the difference of the depth-dose distributions between the inside and outside of the beam center (within the radius of 2.5 cm or not) by setting an r-z mesh.
Change the minimum & maximum values of y axis in the graph for the depth-dose distribution. (set “angel = ymin(XXX) ymax(YYY)” in [t-deposit] tally) (XXX & YYY are the min & max values of the Y axis)
Homework #2

## Slide 73: Example Answer
Homework
Proton (up) and neutron (down) fluences.
Depth-dose distribution inside (up)
and outside (down) the beam radius.